## Slide 1: The TREND update and Nuclear Data Needs for BNL
Date: March 1, 2023
Presenter: Dmitri G. Medvedev

## Slide 2: TREND: TRi-lab Effort on Nuclear Data
Brookhaven National Laboratory (BNL):
  Michael Skulski (postdoctoral), Cathy S. Cutler
Los Alamos National Laboratory (LANL):
  Ellen O’Brien, Christiaan E. Vermeulen, Eva Birnbaum (alumni), Jonathan Morrell (postdoctoral), Francois M. Nortier (alumni, retired)
Lawrence Berkeley National Laboratory (LBNL)/UC Berkeley:
  Catherine Apgar (graduate student), Morgan Fox (alumni), Andrew Voyles, Lee A. Bernstein
Co-authors and collaborators

## Slide 3: Rationale
Knowledge energy dependent cross section is critical for:
Accurate prediction of the yield of the isotope of interest
Accurate prediction of radioisotopic impurities
Defining the energy windows for optimum, cost-effective production of isotopes
It facilitates:
Production planning
Defining shielding requirements
Transportation and shipment constraints
Bonus: comprehensive cross section data sets help constrain nuclear reaction models

## Slide 4: Current state of the field
Most of the data sets are limited to proton energy range up to 30 MeV
A few more data sets are available up to 160 MeV
Limited number of data sets are available up to 200 MeV
A tri-lab collaboration was formed to address the needs and cover proton energy range up to 200 MeV
LBNL/UC Berkeley – 0 - 55 MeV
LANL – 55 - 100 MeV
BNL – 100 - 200 MeV
Seeks to measure nuclear reaction cross sections for production of medically relevant (and other) isotopes and for beam monitor reactions
A comprehensive list of reactions was captured by Dr. François M. Nortier (Meiring) in 2017
Approach

## Slide 5: Data sets of the primary focus
Priority | Isotope | Target | Incident particle | Measurement focus | Energy range | Years
1 | 72Se, 68Ge | 75As | p | Primary: 72Se, 68Ge Impurities: 70,71,73,75Se, 66,67,69,71Ge | Up to 200 MeV | 2019
2 | 119Te, 117mSn | natSb | p | Primary: 119m,119gTe, 117mSn Impurities: 116,117,118,121m,121g,123mTe, 113,119m,121m,121gSn | Up to 200 MeV | 2020-21
3 | 202Pb | natTl | p | Primary: 202m,202gPb Impurities: 198,199,200,201,203,204,205Pb | Up to 200 MeV | 2022
4 | 134Ce | natLa | p | Primary: 134Ce Impurities: 132,133,133,137,139Ce | 50-200 MeV | 2023

## Slide 6: Experimental: stacked foil technique
Irradiate array of target and monitor foils with known thickness/areal density intermixed with degraders
  Very low current 100-200 nA
Use gamma spectroscopy to count each foil individually
  Multiple spectra collection allows for accurate error characterization
Determine activity of all produced radionuclides
Use activation equation to solve for for each individual foil
Degraders
Dr. Jonathan Morrell developed Python based code (Curie)* which performs gamma spectra fitting and decay routine that is used for data analysis
*J. T. Morrell, Curie: Python Toolkit for Experimental Nuclear Data (2020).

## Slide 7: Facilities
BLIP (BNL) and IPF (LANL) share conceptually similar design
  Operate of LINACs
    IPF max accepted proton energy 100 MeV, max current 350 µA
    BLIP max energy 200 MeV, incrementally tunable, max current 200 µA
  Designed for large scale isotope production
LBNL operates 88-inch cyclotron
  Both light- and heavy-ion capabilities.
  Protons and other light-ions are available at intensities (10-20 pA)
  Maximum energies of 60 MeV (protons), 65 MeV (deuterons), 170 MeV (3He), and 130 MeV (4He).

## Slide 8
Brookhaven Linac Isotope Producer (BLIP) target station
Located 30 feet below ground level to the bottom of the water shaft
Targets delivered to and retrieved from the beamline using chain drive system
About 6 inches (152.4 mm) of space available along the beam pass for target positioning
Incrementally tunable LINAC energy: 200, 180, 160, 140, 117, 66 MeV
Rastered and focused beam pattern
Multiple targets arranger stacked one after another
Ground level

## Slide 9: Experimental: stacked foils for irradiation
BLIP
LBNL
IPF

## Slide 10
Morgan Fox LBNL

## Slide 11
Catherine Apgar LBNL

## Slide 12
Michael Skulski BNL

## Slide 13
Jonathan Morrell
LBNL→LANL

## Slide 14: Implications for isotope production
Reactions on arsenic: first data set for natAs(p,x) 68Ge reaction up to 200 MeV revealed opportunities for Ge-68 production with medium to high energy protons
  Lower thermal load on the target at higher energy
  No interference with medium energy production targets at BLIP
Reactions on antimony:
  Control of co-production of long-lived Sn-113 impurity
  Better understanding of energy resolution for Te-118 and Te-119

## Slide 15: Implications for isotope production
Reactions of thallium: comprehensive data sets on thallium will constrain Talys prediction of difficult to measure Pb-202 and Pb-205
Reactions on lanthanum: control of the impurities in production of Ce-134

## Slide 16: BLIP nuclear data needs
BLIP receives 200 MeV protons: this energy has to be absorbed either by degraders or production targets
Cross section data sets with improved uncertainties are necessary for design of both targets and degraders
Data sets for production for energies from 100-200 MeV are of particular importance at BLIP to improve economics of production
Cross section data sets for fast neutrons are of importance due to substantial flux of secondary neutrons

## Slide 17: Acknowledgement
US Department of Energy Isotope Program for funding
Whole-hearted acknowledgement goes to all support personnel of LINAC, Health Physics, engineers, designers
BNL is managed by Brookhaven Science Associates operated by Battelle Memorial Institute (Battelle) and Stony Brook University for US DOE Office of Science.
LANL is managed by Triad LLC, a partnership between Battelle, the Texas A&M University System, and the Regents of the University of California (UC) for the Department of Energy’s National Nuclear Security Administration.
LBNL is managed by University of California for US DOE Office of Science

## Slide 18: The Tri-lab Nuclear Data Collaboration
Not Pictured:
Lee Bernstein (LBNL)
Eva Birnbaum (LANL)
Cathy Cutler (BNL)
Catherine Apgar
Berkeley Nuclear Data Team
Andrew Voyles
Jon Morrell
Morgan Fox
Ellen O’Brien (LANL)
Etienne Vermeulen (LANL)
Meiring Nortier (LANL)
Andrew Voyles (UCB)
Jon Morrell (UCB)
Dmitri Medvedev (BNL)
Morgan Fox (UCB)
Michael Skulski (BNL)