## Slide 1: IAEA Technical Report: Auger electron-emitters for radiopharmaceutical developments
Roger W. Howell
Department of Radiology
Division of Radiation Research
Rutgers New Jersey Medical School
Data Needs & Capabilities for Auger Electron Emitters

## Slide 2: IAEA Report Committee
Julie Bolcaen
  NRF iThemba LABS, Cape Town, South-Africa
Bart Cornelissen
  University of Groningen, Groningen, The Netherlands
Jonathan Engle
  University of Wisconsin, Madison, Wisconsin, USA
Mohammed Gizawy
  Egyptian Atomic Energy Authority, Cairo, Egypt
Roger W Howell
  Rutgers University, Newark, NJ USA
Aruna Korde
  International Atomic Energy Agency, Vienna, Austria
António Paulo
  Universidade de Lisboa, Bobadela LRS, Portugal
Jean-Pierre Pouget
  INSERM, Montpellier, France
Valery Radchenko
  TRIUMF, Vancouver, BC, Canada
  University of British Columbia, Vancouver, BC, Canada
Samantha YA Terry
  King's College London, London, UK
R. No. C0237
Vienna International Centre
Vienna
Austria
5 to 9 September 2022
Ref. No.: EVT 2103627

## Slide 3: Introduction
Auger electron emitting radionuclides
Radiobiology of Auger emitters
AE radiopharmaceutical therapy
IAEA criteria for radionuclide selection
Suggestions for roles of DOE in Auger electron radiopharmaceutical therapy

## Slide 4: Auger Electron Emitting Radionuclides

## Slide 5: Decay Schemes - Auger Electron Emitters
(IC)
(IC)
(IC)

## Slide 6: Densely Ionizing High Linear Energy Transfer (LET) Alpha-particles and Auger-electrons
Wright et al. Radiat. Prot. Dosim. 31, 59-62 (1990).
125I
55Fe
111In
5.3 MeV α-particle
195mPt
Howell et al. Radiat Res 140, 55-62 (1994)
ORNL’s Harvel Wright

## Slide 7: Average Auger electrons/decay
Radionuclide | Physical half-life (d) | Average Auger electrons/decay
Tc-99m | 6 hours | 4
Ge-71 | 11.4 days | 5
Pd-103 | 16 days | 8
In-111 | 2.8 days | 15
Sn-117m | 13.6 days | 14
I-123 | 13.2 hours | 15
Tl-201 | 3 days | 21
Hg-197m | 23.8 hours | 23
Sb-119 | 1.6 days | 24
I-125 | 60 days | 25
Pt-193m | 4.3 days | 26
Pt-195m | 4 days | 33

## Slide 8: Auger Electron Emitters Photon/Electron Ratios (avoid many photons)
Uusijärvi et al. Medical Physics 33, 3260-3269 (2006)
Ra-223 and Y-90 microspheres have been readily accepted in medical practice, in part, because they emit very few photons and therefore considered “safe”.

## Slide 9: Radiobiology of Auger electron emitters

## Slide 10: 125I decays on cell membrane are more effective than decays in cytoplasm
cell membrane
nucleus
cytoplasm
Pouget et al. Radiat Res 170, 192–200 (2008)
But……
Several logs of kill will require >>100,000 decays

## Slide 11: DNA-Incorporated Auger Electron Emitters are more Radiotoxic than Alpha Particles
Howell et al. Radiat. Res. 128, 282-292 (1991)
125IdU, 125IdC
210Po-citrate
5.3 MeV α
37% survival
66 decays
for I-125
9 decays for Po-210
ABSORBED DOSE TO CELL NUCLEUS (Gy)

## Slide 12: Weak Auger Emitters Require More Decays

## Slide 13: The Path to AE Radiopharmaceutical Therapy

## Slide 14: Awakening of Auger Electrons for Therapy
Ludwig Feinendegen
Kurt Hofer (1939-2015)
Jim Adelstein
56 years………

## Slide 15: Circle Back to Key Points Auger Electron Emitters for Therapy
High-LET type radiotoxicity and no dose rate effect
Radiochemistry is “easier” than with alpha emitters
Protectable – primarily classical indirect effects
  implies safety factor relative to alpha particles
Many decays needed to sterilize tumor cells
  use as few decays as possible:
  use radiopharm cocktails to minimize injected activity
    minimizes photons
    minimizes normal tissue toxicity
  prolific Auger electron emitters are preferred

## Slide 16: IAEA Committee Criteria for Prioritizing Radionuclides
Number of Auger electrons per decay
Photon/electron ratio (low photon yield)
Co-emission of conversion electrons and/or beta particles
Normal tissue toxicity (ion should not concentrate in organs)
Physical half-life (preferably 3-20 days)
Targetry and production
  (p,n), (p,xn) most widely available
  d, α, 3He … lesser availability
  Neutron (reactor) low molar activity
  Enriched targets high cost and unreliable supply
Separation chemistry
  Require high chemical and radiochemical purity
  n,y products which decay via β-decay to the desired radionuclide
Vector chemistry
  Chelators
  Require extremely high molar activity due to large number of decays needed

## Slide 17: IAEA Criteria for Selection
#AE/decay | 0-4 | 5-10 | 11-20 | >20
#CE/decay | 0 | 0-1 | 1-2 | >2
%β decay (E) | Present |  |  | None
γ toxicity risk for patient and handlers | High |  |  | None
Imageable (theranostic)* | None | <5% intensity 60-300 keV gammas | 5-50% 60-300 keV gammas | >50% 60-300+ keV gammas or 511 keV PET
Stable daughter (SD) | No | / | / | Yes
Half-life | 12 h < T < 20 d | < 24 hrs | 1-2 days | 3-20 days
Current worldwide availability (WWA) | Not | Limited | In some locations | Widely
Target availability (TA) for radionuclide production | Unavailable or extremely limited | Limited or insufficient enrichment, exorbitant cost | Available but requires enriched or expensive | Widely available and inexpensive
Radiochemistry and separation (RC) | Not currently reported | Challenging | Feasible | Optimized
Chelator availability (CA) | None | Complex radiolabelling | Most likely available | Routine
Molar activity (MA) | Not available without carrier or < 1 GBq/µmol | 1 - 10 GBq/µmol of ligand | 10 - 100 GBq/µmol of ligand | >100 GBq/ µmol of ligand
Vector availability (VA) | No vectors studied |  |  | Considerable number studied
Cellular dosimetry: Self-dose/Total dose ratio (SD/TD) to be defined |  |  |  | 
Bad
Good
Better
Best

## Slide 18: DOE Driven Solutions to IAEA Criteria
#AE/decay | 0-4 | 5-10 | 11-20 | >20
#CE/decay | 0 | 0-1 | 1-2 | >2
%β decay (E) | Present |  |  | None
γ toxicity risk for patient and handlers | High |  |  | None
Imageable (theranostic)* | None | <5% intensity 60-300 keV gammas | 5-50% 60-300 keV gammas | >50% 60-300+ keV gammas or 511 keV PET
Stable daughter (SD) | No | / | / | Yes
Half-life | 12 h < T < 20 d | < 24 hrs | 1-2 days | 3-20 days
Current worldwide availability (WWA) | Not | Limited | In some locations | Widely
Target availability (TA) for radionuclide production | Unavailable or extremely limited | Limited or insufficient enrichment, exorbitant cost | Available but requires enriched or expensive | Widely available and inexpensive
Radiochemistry and separation (RC) | Not currently reported | Challenging | Feasible | Optimized
Chelator availability (CA) | None | Complex radiolabelling | Most likely available | Routine
Molar activity (MA) | Not available without carrier or < 1 GBq/µmol | 1 - 10 GBq/µmol of ligand | 10 - 100 GBq/µmol of ligand | >100 GBq/ µmol of ligand
Vector availability (VA) | No vectors studied |  |  | Considerable number studied
Cellular dosimetry: Self-dose/Total dose ratio (SD/TD) to be defined |  |  |  | 
DOE driven
solutions to increase variety and amount of supply
1
2
3
4
Bad
Good
Better
Best

## Slide 19: IAEA Committee Preliminary List of Radionuclides Considered for Scoring
58mCo 64Cu 67Ga 71Ge 77Br
99mTc 103Pd 103mRh 107Cd 111In
119Sb 123I 125I 125mTe 135La
155Tb 161Tb 165Er 180Ta 189mOs
191mOs 193mPt 193mIr 195mPt 197mHg
201Tl 231Th 237U 239Np
Review article on criteria in preparation.
Julie Bolcaen1#, Mohammed Gizawy2, Samantha YA Terry3, António Paulo4, Bart Cornelissen5, Aruna Korde6, Jonathan Engle7, Valery Radchenko8*, Roger W. Howell9

## Slide 20: Data Needed to Select and Optimize Radionuclide Production
193mPt (example)
  192Pt (n,γ) 193mPt (σ = 2 b)
    Low specific activity due to cold Pt
  192Os (α,3n) 193mPt (next slide)
    Alpha particle energy important for yield and to minimize contaminants
    High specific activity needed to maximize radiation absorbed dose and reduce chemotoxicity of cisplatin

## Slide 21: 192Os (α,3n) 193mPt Cross Section vs E
Uddin et al. Appl Radiat Isotop 68: 2001–2006, 2010

## Slide 22: Suggested Roles of DOE in Auger Electron Radiopharmaceutical Therapy
Explore alternate production pathways
  expand target enrichment capabilities
  calculate/measure cross sections of reaction products
  calculate/measure Auger + ICD electron yields
Increase radionuclide availability to promote research
  expand production capacity
  no cost for funded DOE/NIH research (like beam time)
  low cost for wide distribution
Invest in radiochemistry
  separation chemistry (extract desired radionuclide)
  chelation chemistry
  radiopharmaceutical chemistry

## Slide 23: Acknowledgments to Auger Mentors
Dandamudi Rao
Amin Kassis
Kandula Sastry
(1935-2001)
Jim Adelstein
Fellows
Venkat Narra
Murty Goddu
Ravi Harapanhalli
Mike Azure
De-Yan Hou
Marek Lenarczyk
Anupam Bishayee
Bogdan Gerashchenko
Massimo Pinto
Prasad Neti
John Akudugu
Sumudu Katugampola
Students
Behrooz Vaziri
Jordan Pasternack
Han Wu
Jianchao Wang

## Slide 24: 119Sb = Sastry’s pick for Auger therapy
      Top-rated by
Filosovov …Radchenko https://doi.org/10.1016/j.nucmedbio.2020.12.001
Theranostics? Unfortunately, no photons useful for imaging.
24 Auger electrons / decay

## Slide 25: 165Er = Rao’s Auger emitter
Rao et al. Med Phys 4, 177-186 (1977)

## Slide 26: Rationale for 193mPt
High radiochemical purity of 193mPt
  192Os (36 MeV α,3n : σ = 1.5 b) 193mPt
  0.6% 195mPt (similar characteristics as 193mPt)
No-carrier added
~ 30 Auger electrons per decay
~ 4 day physical half-life
Well studied chemistry (chemotherapy)
Cold platinum available for chemistry development
Potential theranostics imaging (0.11%, 135.5 keV)
Antibody-cis-193mPt ? : Cytometry A. 2016 89(3)292-300.
Howell et al. 4th Int Radiopharm Dosim Symp. pp. 493-513, 1986
Azure et al. https://njms.rutgers.edu/departments/division_radiation/documents/Azure1992_001.pdf
Uddin et al. Appl Radiat Isotop 68: 2001–2006, 2010