## Slide 1: Oak Ridge National Laboratory Experimental Nuclear Data Capabilities and Needs for Isotope Production
Justin Griswold

## Slide 2: High Flux Isotope Reactor (HFIR) and Radiochemical Engineering Development Center enable heavy element production at Oak Ridge National Laboratory
HFIR and REDC began operation in 1965 and 1966, respectively
HFIR operation is expected to continue at least until 2040
High-end aspects of isotope production (heavy actinides, specialty medical isotopes), neutron scattering, and materials irradiation
Unique capabilities for radioisotope separations (>400 isotope shipments annually to universities, hospitals, industry, and other research institutions)

## Slide 3: HFIR: Unique capabilities
HFIR operations are supported by the Office of Basic Energy Sciences in DOE’s Office of Science
Highest thermal flux in Western world
  2.1  1015 n/cm2-s thermal
  1  1014 n/cm2-s epithermal (< 1 MeV)
  4.7  1014 n/cm2-s fast (> 1 MeV)
Brightest cold neutron source in world
Delivers 6–7 cycles per year
Missions:
  Neutron scattering research
  Isotope production
  Material irradiation
  Neutron activation analyses

## Slide 4: Current and emerging radioisotope production at ORNL
ORNL also dispenses high purity 238,239,240,242,244Pu, 237Np, 243Am, 99Tc, 209Po, 233,234,235,238U, and 244,248Cm from inventory
227Ac*
252Cf
225Ac(A/D)*
133Ba
63Ni
75Se
228Th
249Bk
257Fm
89Sr
254/253Es
117mSn*
147Pm
238Pu
191Os*†
192Ir*†
60Co†
177Lu(direct) *†
60Co(crystals)†
195mPt*
229Th*
147Pm*
14C*
210Pb*†
224Ra/212Pb*
188W/188Re*
166mHo*
223Ra/227Th
170Tm*
229Th*
125I †
129I †
230Th†
109Cd*†
177Lu(indirect)*†
In production
Production ready
Proposed / Under development
Emerging
* Limited Production / facilities needed
† ‪‪‪ Cost proposal submitted / in preparation
A/D Accelerator or Decay produced
The production of these radioisotopes is made possible because of the High Flux Isotope Reactor and hot cell processing capabilities at ORNL
33P*
90Sr†
153Gd*†
Notes: 34 isotopes produced/dispensed for DOE IP plus Pu238 for NASA= 35 isotopes

## Slide 5: Neutron Activation Analysis (NAA) Facility
Top Side of Reactor and Beryllium Reflector
Location of NAA PT-1
Contains two pneumatic tube facilities
  PT-1 Thermal Flux 4 x 1014 n cm-2 s-1
  PT-2 Thermal Flux 4 x 1013 n cm-2 s-1
Post-irradiation, PT-1 samples are delivered to a lightly shielded hot cell and PT-2 samples are delivered to a fume hood
Unique set-up for nuclear data experiments involving short-lived radionuclides
Various HPGe detectors are available in the NAA lab for post-irradiation sample analysis
Several are optimized for loss-free counting of short-lived radionuclides

## Slide 6: Np-238 Fission Cross Section
Largest source of heat generation in 237NpO2/Al cermet pellets irradiated in HFIR to produce 238Pu
Short half-life (2.117d), makes experimental measurements difficult
Series of experiments led by C. Romano and D. Glasgow performed at NAA facility (PT-1) to measure 237Np(n,γ)238Np and 238Np(n,f) effective reaction cross sections
1M. B. Chadwick, et. al., ENDF/B-VII.0: Next Generation Evaluated Nuclear Data Library for Nuclear Science and Technology, Nuclear Data Sheets, 107, pp. 2931-3060, 2006.
2M. B. Chadwick, et al., ENDF/B-VII.1 Nuclear Data for Science and Technology: Cross Sections, Covariances, Fission Product Yields and Decay Data, Nuclear Data Sheets, 112, pp. 2887-2996, 2011
3DANON, Y., MOORE, M.S., KOEHLER, P.E., et al., Nucl. Sci. Eng., 1996, V. 124,p. 482.
4ABRAMOVICH, S.A., ANDREEV, M., BOL'SHAKOV, Yu., et al., Proc. of the XIII Meeting on Physics of Nuclear Fission in the Memory of SMIRENKIN, G.M. (Prof.), Obninsk, 1995, p. 303.
5J. D. SPENCER and N. P. BAUMANN, "Measurement of Integral Fission Cross Sections for 238Np," Trans. Am. Nucl. Soc., 12, 284 (1969).2

## Slide 7: Np-238 Fission Cross Section (Cont.)
Effective two-group cross section for 237Np(n,γ)238Np as measured in NAA is close to previously measured experimental data and evaluated data1
  Flux for PT-1 closely monitored with monitor foils before and after irradiation
ORIGEN depletion used as comparison to experimental data
  238Np experimental recovery agreed, 239Np experimental recovery was 30-60% lower2
Supplementary data also needed for fission product harvesting (147Pm, 85Kr, 90Sr etc.)
1Catherine Romano, Ram Venkataraman, David Glasgow & Ben Roach (2022) Measurement of the Effective Capture Cross Section of 238Np in the High Flux Isotope Reactor, Nuclear Technology, 208:11, 1696-1703, DOI: 10.1080/00295450.2022.2070353
2Riley Hunley, Justin Knowles, & David Glasgow (2015), Verification of the 238Np Fission Cross Section for HFIR 238Pu Production. ANS Winter Meeting, Washington D.C.

## Slide 8: How we use nuclear data - HFIRCON
Toolkit to Automate Many HFIR Transport Calculations
  Initial Development to Support 238Pu Production
    Extends many code improvements initially developed for large ITER analyses
  Final Product Intended to Support Numerous Other Analyses
    Materials Testing, Isotope Production, Target and/or Core Design
S. C. Wilson et al., HFIRCON Version 1.0.5 User Guide, ORNL/TM-2020/1742 (2020).
    Heat generation rates
    Cycle length calculations
    Supports HFIR target safety bases

## Slide 9: HFIRCON Nuclear Data Needs
Reaction Cross Sections for New Isotope Production Campaigns (recently added (n,g) xs for 187W/188W and 228Ra)
  Reaction cross sections for ORIGEN depletion
    Full evaluation with scattering and secondary particle production not needed for ORIGEN
Best Available Gamma Production Data (GPD)
  Local heat generation rates can be off significantly in isotope production or materials testing targets
    With no GPD, photon energy from (n,X) reactions remains local to the target
    For light elements much (95+ % in some cases) of the gamma energy is absorbed outside of the region of interest
    Even for heavier elements (e.g., tungsten) roughly half of the gamma energy may be transported out of region of interest
    For a portion of the HFIR control elements, local heating rate calculations were conservative by roughly 5x due to missing GPD

## Slide 10: Heavy Actinide Nuclear Data Needs
251Cf
36%
252Cf
245Cm
250Cf
250Bk
249Bk
249Cm
248Cm
247Cm
246Cm
244Cm
244Am
243Am
243Pu
242Pu
241Pu
240Pu
239Pu
26%
10%
Fission
products
Fission products
Fission
products
0.8%
Fission
products
0.4%
Fission
products
64%
0.3%
8.5%
1.5%
D.E. Ferguson, A. Chetham-Strode, and J. R. McWerter, ORNL-TM-165, P. 13 (1962).
~5-10% uncertainty in absorption cross sections of most Cm-Cf isotopes
Uncertain resonance energies
Critical to production of Bk, Es, Fm isotopes used in superheavy element synthesis
251Cf Absorption Cross Section
Blue: ENDF/B-VIII.0
Green: JEFF-3.3
Red: ROSFOND-2010

## Slide 11: Additional Needs
Inelastic neutron scattering data for 117Sn(n,n’)117mSn and 195Pt(n,n’)195mPt reaction cross sections
Confirmation of 229Th fission cross section
  Largest component of heat generation for HFIR production of 227Ac and 229Th through irradiation of 226RaCO3/Al cermet pellets
W and Os cross sections related to 188W production in HFIR through the irradiation of enriched 186W rings
Gaps in available nuclear data are routinely discovered as new isotope production campaigns begin

## Slide 12: How can we help the nuclear data community?
Focus is on isotope production
Data is generated as a coproduced byproduct of isotope production campaigns
Geometry is not ideal for nuclear data experiments
  Self-shielding, flux depression etc.
In-situ flux monitoring is not common
Database of experimental data with corresponding theoretical models with accurate experimental geometry?

## Slide 13
Acknowledgements
This research is supported by the U.S. Department of Energy Isotope Program, managed by the Office of Science for Isotope R&D and Production.
Mitch Allmond
Rike Bostelmann
Chris Bryan
David Chandler
Roy Copping
Charles Daily
David Glasgow
Julie Ezold
Susan Hogle
Riley Hunley
Ben Roach
Cathy Romano
Ram Venkataraman

## Slide 14
Thank You!

## Slide 15: CLARION Detector System
Compton suppressed HPGe detectors
Useful for detecting low-intensity gamma ray emissions within high background
Can perform γ-γ coincidence measurements
Used recently in detection of 229Pa(t1/2 = 1.5 d) from 232Th(p,4n)229Pa reaction
  229Pa decays to valuable medical radionuclide 229Th
  Experiment performed at 88-inch cyclotron at LBL
Precursor to FSDi detection system being installed at FRIB