## Slide 1: Ray Hafalia, LBNL TFD Preliminary Design Review February 16, 2023
TFD Magnet Structural Design
And Assembly Tooling

## Slide 2: Major Subassemblies
1.0 Coil Winding & Reaction Fixture
2.0 Coil Reaction Fixture-in-Retort [Conceptual]
2.0 Coil Module
3.0 Coil Pack
4.0 Shell – Yoke Structure
5.0 Magnet Top Assembly

## Slide 3: Coil Winding and Reaction Fixture [To be covered, in detail, in “Coil Parts & Fabrication Tooling”, Jose Luis]
Upgraded Winding Table
Reinforced existing infrastructure.
[Concept shown]
Reaction Base Plate Assy
Weight: 430 KG [948 lbs].
Coil 1 Reaction Fixture
Weight: 2195 KG [4841 lbs].

## Slide 4: Coil Reaction Fixture in Retort [Preliminary design, as initially shown by Diego]

## Slide 5: Coil Module
Inter-Coil Smart Shim
Inter-Coil Spacer (Stainless Steel)
Wedge (Stainless Steel)
Coil 1
Vertical Load Pad Spacer (Stainless Steel)
Vertical Load Pad
Assembly Support Fixture [Conceptual]
Mid-Plane Smart Shims
Coil 2

## Slide 6: Coil Module
Coil Module Weight: 1213 kg [2675 lbs]

## Slide 7: Coil Pack
Coil Modules
Assembly Support Fixture
Mid-Plane Smart Shims
Horizontal Load Pads
Vertical Load Pads
Coil Pack Weight: 3496 kg [7709 lbs]

## Slide 8: Coil Pack
End Caps
Stainless Steel
Vertical Load Pad Assembly
Weight: 431 kg [951 lbs]
Center Laminations
ARMCO Steel (Ferrous)
Horizontal Load Pad Assembly
Weight: 535 kg [1180 lbs]
End Caps
Stainless Steel
Center Laminations
ARMCO Steel (Ferrous)
Bushings
Stainless Steel

## Slide 9: Shell & Yoke Structure
Yoke Stack (2)
ARMCO Steel Laminations
Weight (ea.): 5435 kg [11982 lbs ]
Aluminum Shell (2)
7075-T6 Aluminum
Weight (ea.): 957 kg [2109 lbs ]
Shell & Yoke Structure
Assembly Weight: 12798 kg [28215 lbs ]
Note: All ARMCO Steel laminations are of the same thickness. The 2 outer laminations at both ends are machined thinner to bring the overall length of the assembly to 2.00 meters
Bushings
Stainless Steel
Yoke Gap Keys (2)
Stainless Steel

## Slide 10: Magnet Top Assembly
TFD Magnet Top Assembly
Weight: 18100 kg [39910 lbs ]
Vertical Load Keys
Horizontal Load Keys

## Slide 11: Magnet Top Assembly
Shell & Yoke Structure
Weight: 12798 kg [28215 lbs ]
Axial Rods (4)
Stainless Steel
Weight (each): 106 kg [234 lbs]
Coil Pack Assembly
Weight: 3496 kg [7709 lbs]
RE End Plate
Nitronic 40
Weight: 609 kg [1343 lbs]
LE End Plate
Nitronic 40
Weight: 525 kg [1157 lbs]

## Slide 12: Magnet Top Assembly
Vertical Preload of Coil Pack
Bladder operations are performed from the return end of magnet.
Horizontal Preload of Coil Pack
Bladder operations are performed from the lead end of magnet.
Vertical Bladders and Keys
Horizontal Bladders and Keys

## Slide 13: Reference Assembly Drawing for HFVMTF [Slide supplied by GianLuca]

## Slide 14: End Presentation

## Slide 15: Magnet Installation in the HFVMTF Cryostat Header
Extra Slide