## Slide 1
Shlomo Caspi
US Magnet Development Program
Lawrence Berkeley National Laboratory
Hybrid magnet design

## Slide 2: CCT conceptual dipole design
Magnetics
  19 T – Lorentz forces
    6 layers
    Any conductor – Nb3Sn, HTS (carrying the same current)
Internal Structure
  CCT spars
  Assembly/Disassembly
External structure
  Yoke and Shell

## Slide 3: Lorentz Force – Back to basics
An isolated turn at 20T
pre-stress
coil bending
We want a turn in a box

## Slide 4: 19 T CCT dipole
More than 60 mm of wide conductors needed for 6 layers
Layers snuggly fit
“Smart-shims” are used for assembly and disassembly
Internal Structure - Lorentz forces are transferred to spars.
External Structure – prevent layers bending by an iron yoke

## Slide 5: Internal structure
spar
“smart-shim”
Layer (mm)
1 Ri = 25
Ro= 37.6
2 Ri = 38.6
Ro= 51.2
3 Ri = 52.2
Ro= 71.2
4 Ri = 72.2
Ro= 91.2
5 Ri = 92.2
Ro= 107.2
6 Ri = 108.2
Ro= 123.2
shell -1 Ri = 124.2
Ro= 134.2
Shell-2 Ri = 260
Ro= 325
All spars are 3 mm
Layer to layer gaps 1mm
All smart-shims 80 deg.

## Slide 6: 19 T, 14 kA/turn

## Slide 7
Magnet Assembly

## Slide 8: The CCT magnet
Each layer is machined, wound, reacted and impregnated separately
6 layers are assembled using “smart-Shims”
A thin Aluminum shell is placed over layer 6
An iron yoke is placed over the coils and held by an Aluminum shell
“smart-shims” take care of any geometry irregularity between layers and function similarly to “keys and bladders”

## Slide 9: Assembly using “Smart-Shims”
5 KN/m ~ 5 microns
Insert layer 1 into layer2 (~1mm radial gap)
Layer 2 is bent, a “smart-shim” inserted, epoxy injected, curing, layer 2 springs back
The two layers are fitted snugly (not bonded)
Process continuous for all layers
By reversing the process the layers could be disassembled
GAP

## Slide 10: Placing CCT layer 1 into 2
~1 mm gap
Clamps used to deform layer 2

## Slide 11: “smart-shim” removed

## Slide 12: Bend layer 2
Radial Displacement (m)
Scale factor 1000
Layer 2, 3.1 microns

## Slide 13: Inflate shim between layers 1-2
Radial Displacement (m)
Scale factor 1000

## Slide 14: Release Layer 2
Scale factor 1000
Layer 2, 2.9 microns

## Slide 15: Release shell-1
Scale factor 1000
Shell-1, 5.4 microns

## Slide 16: Displacements -- Shims + conductor
Scale factor 1

## Slide 17: Azimuthally stressed conductor - RT
Scale factor 1
Less than 2 MPa

## Slide 18: Azimuthally stressed conductor - Cold
Scale factor 1
All under compression
-17 to -141 MPa

## Slide 19: Azimuthally stressed conductor – 19T
Scale factor 1
+65 to -167 MPa

## Slide 20: Radial stressed conductor – 19T
Scale factor 1
+17 to -145 MPa

## Slide 21: Azimuthally stressed inner structure – RT
Scale factor 1
6 to -4 MPa

## Slide 22: Azimuthally stressed inner structure – cold
Scale factor 1
+146 to -516 MPa

## Slide 23: Azimuthally stressed inner structure – 19T
Scale factor 1
All under compression
+328 to -668 MPa

## Slide 24: Structural shells - RT
Scale factor 1
Low ~ 1 MPa

## Slide 25: Structural shells - cold
Scale factor 1
+396 to -145 MPa

## Slide 26: Structural shells – 19T
Scale factor 1
+430 to -26 MPa

## Slide 27: Structural Yoke – cold
Scale factor 1
+28 to -350 MPa

## Slide 28: Structural Yoke – 19T
Scale factor 1
+74 to -531 MPa

## Slide 29: Conclusions
Magnet assembly using “smart-shims”.
Internal structure to integrate Lorentz forces in spars.
External structure to prevent internal bending

## Slide 31: Layer 1- coil Azimuthal Stress (MPa)
Assembled cold 19T
Sy (MPa) = +60, -100 cold = +30, -30 19T =+80, -40