## Slide 1
Lucas Brouwer
US Magnet Development Program
Lawrence Berkeley National Laboratory
CCT4 Modeling and Test Results
February 8th 2018
2nd MDP Collaboration Meeting: Jacksonville, Florida

## Slide 2: Introduction
Overview:
  mechanical modeling of CCT4 shows potential trouble areas
  overlaying acoustic data with modeling results
  comparison of strain gauge data between tests and with ANSYS

## Slide 3: Overview of CCT4 ANSYS Models
“Improved Modeling of Canted-Cosine-Theta Magnets”, IEEE Trans. Appl. Supercond., PP 99, Nov. 2017
2D 3D periodic 3D full
2D
- design of external structure
- limited parametric studies
3D periodic
- 3D conductor stress state
- circuit-coupled protection study
3D full
- choice and validation of 3D periodic boundary conditions
- critical for understanding test results from short magnets (CCT3,4,5)
3D full results will be shown

## Slide 4: Mechanical Behavior of Interfaces is Important for the CCT
4
layer of epoxy around conductor (brown)
element coordinate system alignment allows for anisotropic conductor and epoxy (warp,fill,normal) properties
Epoxy interfaces are a possible source of quenches
between cable and channel
between layers
and b/w layers

## Slide 5: Trouble Spots for Correlation with Acoustic Measurements
#1: large conductor-channel shear at +- 45 deg
#2: large shear between layers at pole of bonded model
Sxz
Syz
Where should we look for trouble? Where is the epoxy likely to fail first?

## Slide 6: Overlaying Acoustic Data and Modeling Results – Interlayer Shear
See Diego’s talk for a new assembly method to better define layer interface (Bend+Shim)

## Slide 7: Overlaying Acoustic Data and Modeling Results – Conductor Shear
No strong conclusions yet, but we are using modeling to help guide our search (more in Maxim’s talk)

## Slide 8: Strain Gauge Data: First Test of CCT4
Compare CCT4 test to full 3D ANSYS model with bonded vs. sliding
Strain gauges are mounted on the aluminum shell at the pole (POL) and midplane (MID) in both azimuthal (T) and axial (Z) directions
Strain gauges during powering are similar to ANSYS prediction

## Slide 9: Strain Gauge Data: Thermal Cycle of CCT4
All of thermal cycle ramps vs. the final ramp from the CCT4 initial test
Gauge readings are still linear and the same as before the thermal cycle (no significant change)

## Slide 10
Extra Slides

## Slide 11: Contact Shear at Layer to Layer Interface
Layer to Layer Bonded
Layer to Layer Sliding
Peak shear location moves from pole to midplane depending on layer interface property (bonded vs. friction)

## Slide 12: Overlaying Acoustic Data and Modeling Results – Interlayer Shear (First 20)

## Slide 13: CCT4 Local C.S. Stresses at Short-Sample Current
tangent
radial
binormal
tangent-radial
tangent-binormal
radial-binormal