## Slide 1: T-Production Session Summary
Paul Humrickhouse (ORNL)
Stephanie Lyons (PNNL)
Sofia Quaglioni (LLNL)
Notes: Image: Abstract Data Visualization – Stock Photo

## Slide 2: Overview
Fusion reactors are anticipated to breed the tritium needed to fuel energy production. However, quantities of this isotope will be needed during reactor startup, and it may be in short supply.
Are there production processes or reactor materials that can be used to establish a source of tritium for fusion energy applications?
Which nuclear data are necessary to support testing and operation of liquid blankets? Ceramic blankets?
What are the uncertainties and sensitivities to tritium breeding ratio?
Is the accuracy of nuclear data sufficient to predict activation of breeder blankets?
Nuclear reactions will contribute to chemical changes in breeder blankets. Can nuclear cross sections be used to accurately predict transmutation of materials in blankets?

## Slide 3: Topics Discussed
Tritium Breeding Blanket Design and Materials
NNSA Tritium Modernization Program
Challenges to Achieving Tritium Self-Sufficiency
Advanced Reactors and Accelerators: Alternative Pathways for Tritium Production
Measurements of Neutron-Induced Breakup Reactions from Lithium Isotopes with Fast Neutrons Using an Inertial Confinement Fusion Platform
Predictive theory for T production
Utilization of a High-Flux DT Neutron Source for Tritium Breeding Experiments
Integral Experiments for Tritium Production
Stakeholders:
DOE NNSA, Defense Program
DOE SC- FES, NP

## Slide 4: Findings (I)
Shared interest from NNSA Tritium Modernization Program for T production at current reactors and future advanced reactors
  A variety of light-ion reactions beyond n+Lithium and n+Beryllium are important to their accountancy
Sustained operation of fusion reactor must be provided by a breeding blanket
  Fuel cycle may require TBR > ~1.15
  Penetrations and other components may reduce TBR by 0.1 – 0.15
  Nuclear data uncertainties in TBR may be as low as ~3% to as high as ~15%
  Few studies available are not for US blanket designs

## Slide 5: Findings (II)
Breeding blankets ingredients:
Tritium Breeding (n,T): Li, with variable enrichment in 6Li
Neutron Multiplication (n,2n): Be, Pb
Combinations:
  Liquid metal (Li, PbLi)
  Solid (Li2TiO3 or Li4SiO4 + Be or Be12Ti)
  Molten Salt (FLiBe)
Structural Materials:
  RAFM Steel (e.g. Fe+8Cr+2W+0.2V+0.04Ta)
  Vanadium alloys (e.g. V-4Cr-4Ti)
  SiC composites
Coolants: Helium, Water
Other important materials: Tungsten (PFCs, FW armor, stabilizing shells, etc.)

## Slide 6: Findings (III)
Fast-neutron region (2-14 MeV) is important!
Propagation of nuclear uncertainty important for accurate estimation of TBR
  Methods: perturbation theory, probabilistic random sampling (TMC)
  Reliable covariance data needed for the perturbation theory method (covariance data missing or incomplete)
  Random nuclear data files for all nuclides needed in TMC methods (randomized nuclear data files not generally available)
Solid breeder TBR uncertainty seems to be dominated by 6Li and 16O
  More studies are needed!

## Slide 7: Findings (IV)
Light-ion evaluations need improvements, lack covariances; Experimental data for fast neutrons are limited, discrepant.
  Need theoretical tools to describe reactions with multiple outgoing fragments
  Need additional measurements to constrain theory, evaluations
  Need well-evaluated uncertainties to pass on to transport codes
Evaluations based on predictive theory possible with advanced HPC architectures, are better suited to dealing with absent or incomplete data
LLE (OMEGA), SHINE, NIF are facilities that would enable differential/integral measurements
There are no (sanctioned) integral benchmarks for fusion breeder blankets
  Some benchmarks with 6Li with neutron spectrum from fission
  None for fusion neutron spectrum!

## Slide 8: Preliminary Recommendations
More detailed scoping study to identify gaps in existing data and set priorities
Sensitivity studies for various US reactor and breeder designs
  PbLi cooled, Dual Cooled Led-Lithium (DCLL); FLiBe
  Readiness of transport codes? Are there gaps in processing codes?
  Translate FENDL into GNDS format to enable broader sharing of information across communities
  How can nuclear data improvements help improve TBR uncertainties?
Assessment of existing differential data combined with predictive simulations, R-matrix analyses to improve evaluations, identify new measurement needs
  Cross-sections, angular distributions, exit-channel product information in fast neutron energy regime
  Covariances
  Identify new measurements needed to resolve nuclear data issues
Build a path toward integral benchmarks for fusion neutrons
  Survey existing diagnostic data from labs, other programs
  Leverage current facilities to establish initial integral benchmarks for blanket subassemblies
  Work to define best benchmarks for US blanket designs