## Slide 1: Wanted: Tiny radioactive samples for neutron transmission measurements with DICER at LANSCE
LA-UR-24-21823
Experiendo cognoscitur
Th. Stamatopoulos1, P. Koehler1, A. Couture1, G. Rusev2
V. Mocko2, E. Vermeulen2, E. O’Brien2
B. DiGiovine3
Physics Division, Los Alamos National Laboratory, 87545, NM, USA
Chemistry Division, Los Alamos National Laboratory, 87545, NM, USA
Weapons Stockpile Modernization Division, Los Alamos National Laboratory, 87545, NM, USA

## Slide 2
The why
Notes: This is the chart of nuclides. Each little square represents a nucleus with a given combination of number of neutrons (N, the horizontal axis) and protons (Z, the vertical axis). The black squares represent stable nuclei and it’s what we call the valley of stability. As a general rule of thumb, the further away we move from the valley of stability, the smaller the half like of the nucleus. Now let’s zoom in a random region.

## Slide 3
The why
(n,γ)
(n,2n)
Notes: Again the black nuclei are stable and the rest are radioactive. Their half life is shown under their name. The “pink” nuclei disintegrate by electron capture or b+ and they “transform” themselves in the lower right nucleus or in bottom-right diagonal element indicated with the arrows.
An important element is to know the production and destruction rates of certain nuclei when they happen to be in a neutron field. There are two basic ways to destroy and produce certain nuclei. You can absorb a low energy neutron (i.e. E<1 keV) and then spit out gamma rays and that moves you to the next right nucleus or absorb a high energy neutron (E > 10 MeV) and then spit out 2 or more neutrons (n,2n) which moves you to the nearest left nucleus. The better you know the production/destruction rates known as cross sections, the better you can predict what will happen in a dynamic environment.

## Slide 4
The what-we-know
Notes: This work is focused on the (n,g) process. Measuring neutron capture rates it not trivial for radioactive nuclei. Just for fun look at the known (n,g) cross section for 25meV neutron energy. All the grey boxes are unknown. The gray squares are typically radionuclides.

## Slide 5
The how-we-wish
Notes: The reason this is difficult is, in typical (n,g) experiments, the nucleus under study, is placed very close to gamma detecotrs. So the gamma rays from the disintegration can mix up with the gammas from (n,g). We developed an indirect way to measure capture rates when other techniques fail.

## Slide 6
The how-we-can
Notes: Instead of capture we can study the transmission of neutrons through nuclei and from that we can deduce or extract the neutron capture cross section. This is what the Device for Indirect Capture Experiments on Radionuclides does or DICER.I won’t go into details because this session is focused elsewhere. What I’ll say though is that in these experiments the sample thickness is a very important parameter. You need a certain thickness to acquire good data. Also keep in mind that when you want to study radioactive samples you have to think about the dose rates the personnel will be exposed to and also the difficulty of fabricating large amounts of material. IN other words, there’s a mass limitation. Given the certain length that’s required, you need to make samples with small diameter. What I’m showing here is DICER and long story short is that it’s an instrument with a very precise and sophisticated collimation system that measure the transmission of neutrons through a sample. This instrument is designed to study very tiny amounts of materials that span from ng to a few mg. Currently we can measure samples with 1mm diameter and we are going to switch to 0.1mm. And this where you take it.

## Slide 7
The where
LANSCE@LANL
1st takeaway: walking distance from IPF!
2nd takeaway: A few minutes drive to the hot-cells.
Notes: Instead of capture we can study the transmission of neutrons through nuclei and from that we can deduce or extract the neutron capture cross section. This is what the Device for Indirect Capture Experiments on Radionuclides does or DICER.I won’t go into details because this session is focused elsewhere. What I’ll say though is that in these experiments the sample thickness is a very important parameter. You need a certain thickness to acquire good data. Also keep in mind that when you want to study radioactive samples you have to think about the dose rates the personnel will be exposed to and also the difficulty of fabricating large amounts of material. IN other words, there’s a mass limitation. Given the certain length that’s required, you need to make samples with small diameter. What I’m showing here is DICER and long story short is that it’s an instrument with a very precise and sophisticated collimation system that measure the transmission of neutrons through a sample. This instrument is designed to study very tiny amounts of materials that span from ng to a few mg. Currently we can measure samples with 1mm diameter and we are going to switch to 0.1mm. And this where you take it.

## Slide 8
A few specs
Cylinder
1 mm or 0.1 mm diameter
1.5 cm in length
Powder sample, stuffed in a capillary tube, plugged with Al wire and placed inside an Al DICER canister
Powder
Al plug
Capillary tube
Liquid radioactive 88Zr sample, dispensed in a W canister
Metallic sample (Mo, Cd, Gd) in an Al screw down canister.
Liquid, powder and metallic samples.
Sample canister: 1.5 cm long, 1 cm diameter
Cryogenic and gaseous targets are on the works
Al canister with a pass-through hole
Notes: This is a synergy between physics, chemistry, radiochemistry and engineering. We nailed out the physics and the engineering of the instrument so we know how to do experiments and analysis. Each new measurement we want to do is a research project by itself and requires brainstorming between physics, chemistry and engineering. I’ll give you a few examples of some of the specs that go on the table and are actually the starting points of discussions.

## Slide 9
A few more specs
Samples should fit the DICER sample format (1/0.1 mm diameter, 1.5 cm length)
Uniformity and homogeneity
Minimization of hydrogen: replacement with deuterated compounds(?)
Other components in the sample, should be transmission friendly: Avoid nuclei that are neutron absorbers.
1 mm diameter, 1 cm length
Water vs Heavy Water
Deuterium
Hydrogen

## Slide 10
A few more specs
Samples should fit the DICER sample format (1/0.1 mm diameter, 1.5 cm length)
Uniformity and homogeneity
Minimization of hydrogen: replacement with deuterated compounds(?)
Other components in the sample, should be transmission friendly: Avoid nuclei that are neutron absorbers.
1 mm diameter, 1 cm length
Water vs Heavy Water
Deuterium
Hydrogen
150 ug 88-Y sample
88-Y
14-N
2-H
16-O
Total: Y(NO3)3 + 6D2O 2M DNO3

## Slide 11
The curious case of 88Zr (t1/2 = 83.4 days)
LLNL: σγth = 0.861(69) Mb Shusterman et al., Nature 565, p 328 (2019)
LLNL: Iγ = 2.530(280) Mb Shusterman et al., PRC 103 124614 (2021)

## Slide 12
DICER-IPF synergy: The 88Zr case aka a success story
The radioactive sample fabrication relies on the synergy between LANSCE and IPF
Proton irradiation of a suitable bulk material (89Y)
Chemical separation and purification (600 mCi, 10 mL 88Zr + H2O●6mol/L HCl )
Gamma spectroscopy to extract mass
A. Matyskin et al, Sci. Rep., 2023 13(1), 1736
A. Stamatopoulos et al., J Rad. Chem., 2022, 331(12)
A. Stamatopoulos et al., EPJ., Conf. 260, 03006 (2022)

## Slide 13
Development of filling station
To enclose our 88Zr liquid sample, we developed a filling station that was remotely operated in the hot cells and dispensed the material in W cans.

## Slide 14
Development of a 0.1 mm collimator : 88Y case
Need for 0.1 mm-diameter samples: Development of a new 0.1 mm collimator

## Slide 15
Development of a 0.1 mm collimator
Need for 0.1 mm-diameter samples: Development of a new 0.1 mm collimator

## Slide 16
Development of inkjet printing
Inject printing of radioactive samples is a possibility we are currently exploring
This will hopefully allow to print samples with a small diameter (i.e. 88Y)

## Slide 17
Development of inkjet printing
We managed to print NaCl, some Vanadium salts and YOCl.
NaCl on Au substrate
NaCl on silicon substrate; different printer settings
NaCl on plastic substrate

## Slide 18
Development of microjet printing
Inkjet printing of radioactive samples is a possibility that LENZ and DICER are currently exploring

## Slide 19
Development of microjet printing
YOCl ink printed on Zr substrate by Scott Essenmacher

## Slide 20
A few future nuclides we would like to study
Nuclide | Half-life
88Y | 106.6 days
107Pd | 6.5 106 years
134Cs | 2.065 years
147Pm | 2.62 years
152Eu | 13.52 years
155Eu | 4.75 years
153Gd | 240.4 days
163Ho | 4570 years
170Tm | 128.6 days
185W | 75.1 days
186Re | 3.72 days
192Ir | 73.8 days
193Pt | 50 years
Nuclide | Half-life
3H | 12.3 years
171Tm | 1.92 years
151Sm | 90 years
2H | stable
133Cs | stable
40Ar | stable

## Slide 21
Thank you for
your attention!

## Slide 23
9Back-up slides

## Slide 24
Press that we used to seal the 88Zr sample

## Slide 25
The Pb seal we used on the 88Zr sample
The press deformed the Pb shot