## Slide 1: Fission product yield measurements using 252Cf spontaneous fission and neutron-induced fission on actinide targets at CARIBU
February 29th 2024
Guy Savard
Argonne National Laboratory and University of Chicago

## Slide 2: ATLAS/CARIBU facility
DOE Nuclear Physics national user facility
Stable beams at high intensity and energy up to 10-20 MeV/u
Light in-flight radioactive beams with RAISOR
  light beams, no chemical limitations, close to stability, acceptable beam properties
CARIBU beams
  heavy n-rich from Cf fission, no chemical limitations, low intensity, ATLAS beam quality, energies up to 15 MeV/u
State-of-the-art instrumentation for Coulomb barrier and low-energy experiments
Operating ~6000 hrs/yr (+ 2000 hrs/yr CARIBU stand alone) at > 90% efficiency
  Common PAC for ATLAS and CARIBU
  300-400 “single users” per year performing experiments at ATLAS

## Slide 3: Fission fragment yield information
Fission produces hundreds of neutron-rich fission fragments. These isotopes have different lifetimes and chemical properties
The fission fragment distribution experimental information is mostly obtained on longer-lived isotopes through decay measurements. Yield for shorter-lived isotopes is mostly from modeling to reproduce the measurement on longer-lived isotopes.
Quantitative knowledge of the decay properties of these isotopes is critical for most of these measurements.
This data is at best unreliable … we have a number of projects (many at CARIBU) to improve this information on medium and shorter-lived isotopes to support the measurement techniques based on decay radiation detection, but this is not the topic of this talk.
We have developed a new approach for these measurements that works by detecting isobarically selected ions to directly determine the yield. This technique is essentially independent from the chemical properties of the isotope and can be applied to isotopes with half-life down to ~ 25 ms.

## Slide 4: Of unique interest for nuclear data: Neutron-rich beam source for ATLAS
Main components of CARIBU
PRODUCTION: “ion source” is 252Cf source inside gas catcher
    Thermalizes fission fragments
    Extracts all species quickly
    Forms low emittance beam
SELECTION: Isobar separator and MR-TOF
    Purifies beam
DELIVERY: beamlines and preparation
    Low-energy buncher and beamlines
    Charge breeder to Increase charge state for post-acceleration
    Post-accelerator ATLAS and weak-beam diagnostics
Commissioned in 2020
Commissioned in 2017
Commissioned in 2012

## Slide 5: CARIBU Californium rare isotope breeder upgrade
RFQ prep trap
Penning
trap
Position-sensitive MCP
252Cf
~0.5 Ci
R = m/Δm ~ 10,000
R ~ 100,000
R ~ 20,000,000

## Slide 6: MR-TOF Multi-reflection time-of-flight mass separator
System built to be isochronous with respect to energy …. i.e. Dt / DE = 0
Keep time dispersion from mass difference
V
d
E + DE
E
E - DE

## Slide 7: Phase-Imaging Ion Cyclotron Resonance (PI-ICR) method in the CPT Penning trap spectrometer
With this method we are measuring the sum of the two orbital frequencies.
Originally developed off-line by S. Eliseev et al, PRL 110 (2013) 082501
We have demonstrated resolution of over 10,000,000 allowing to easily separate isomers

## Slide 8: PI-ICR mass separation

## Slide 9: MR-TOF + PI-ICR Beam of A/q = 150/2+
Pr
Ce
CeH
La
LaH
MR-TOF is a crucial device for the CPT
What does R = 100,000 really mean?
Moving 300ns BNG window around allows us to select a single isobar and suppress others

## Slide 10: Ion counting Isomer measurements: fission yield, excitation energy, ….
156Pm , Tacc = 234.705 ms
162Tb, Tacc = 125.241ms
168Tb, Tacc = 234.247ms
A number of results related to the influence of these isomers on nuclear structure and astrophysics (astromers) have already been published … a big compilation of 252Cf fission isomeric yield is coming.

## Slide 11: Ion counting for fission yield: use shorter excitation ( ~ 4 ms) and probe various angles
Tacc =4.212 ms
Tacc =4.232 ms
Tacc =4.242 ms
Tacc =4.252 ms
clustering algorithm

## Slide 12: Completing analysis for spontaneous fission yield of 252Cf
Lots of data … still very preliminary, but looks like old E&R table as good as new table
Tables underestimate production of the most n-rich isotopes
Preliminary …

## Slide 13: Next step is n-induced fission: nuCARIBU
Neutron induced fission of actinide foils
Replace the 252Cf source and infrastructure with p+ cyclotron, transport, and targets
p-7Li reaction for neutron production
Chicane provides room for cyclotron ion source and enables shielding at 180°
nuCARIBU

## Slide 14: nuCARIBU progress
Cyclotron positioned in CARIBU June 2023

## Slide 15: nuCARIBU progress
Mechanical and RF installation Nov-Dec 2023

## Slide 16: nuCARIBU progress
Transport magnets delivered; chicane assembled off-line and ready for installation
Neutron production target heat exchanger fabricated and undergoing testing

## Slide 17
Independent fission yield measurements status
Isobar resolution with MR-TOF
The technique we have developed relies on the universality of the CARIBU extraction system and high-resolution mass separation followed by ion counting. The technique is fast and insensitive to lack of, or incorrect, decay information.
We are finishing the analysis of the isomer ratio yield and independent fission product yield for spontaneous fission of 252Cf. Still some data being taken to complete evaluation but essentially completed.
Preparing to shift to nuCARIBU where we can use the same technique to look at FPY for thermal neutron induced fission on 235U and 239Pu. This will allow direct measurements on n-induced fission fragments with sub-second lifetime … those are critical for a number of applications and have only been determined indirectly so far.
Isomer resolution with Penning trap

## Slide 18: Next big step for spectroscopy of fission fragments : Gammasphere move to area 1
Current status: Gammasphere is located in area 4 – reacceleration of the CARIBU beam through the ATLAS facility is needed
  loss of beam intensity – 10
  unable to use the unique MR-TOF capabilities – loss of unambiguous separation of isobars
What we are preparing: move Gammasphere to area 1 and perform dedicated studies of high-priority cases – WoNDRAM & IAEA high-priority lists

## Slide 19: Supplementary material

## Slide 20: CARIBU beams delivered to experiments so far
All of these beams now available in the new low-background low-energy area (Area 1)