## Slide 1: A Bayesian Approach to Radiation Image Reconstruction and Uncertainty Quantification
NSD Meeting – Mar. 5, 2024
Jaewon Lee — jwonlee@berkeley.edu

## Slide 2
Outline
Introduction — Scene Data Fusion / Single Detector Imaging
Gaussian Process Prior (GPP) for Image Reconstruction
Bayesian Uncertainty Quantification
Simultaneous Full Spectral Imaging and Spectral Decomposition

## Slide 3
Single Detector Imaging - Introduction
Compton imaging
Radiation Imagers
Coded aperture imaging
Co-60 Imaging using a Compton camera
†
† https://h3dgamma.com/
Notes: Img source https://www.sciencedirect.com/science/article/pii/S0168900209012819
Todo read about some Compton Imaging reconstruction algorithm (Don’s paper, Dan xu’s paper, )

## Slide 4
Single Detector Imaging - Introduction
Simultaneous Localization and Mapping (SLAM)
LiDAR
Radiation Imagers
SLAM, Odometry
Stereo camera \ IMU
†
† BLAM, https://www.youtube.com/watch?v=08GTGfNneCI
Notes: So first I’ll start with a brief introduction. Radioactive source imaging is an important task with many applications related to nuclear safety and security, such as accident remediation, lost source search, and accident response. And many different radiation imagers with different concepts have been developed in the past, such as Compton imager or coded aperture.
On the other hand, what we have today is this enormous advance in computer vision technology, such as Simultaneous localization and mapping, using lidar and stereo camaras.

## Slide 5
Single Detector Imaging - Introduction
Polaris-LAMP
Radiation Imagers
SLAM, Odometry
Scene Data Fusion (SDF)
Free-moving, 3D radiation imaging
†
† J. Hecla et al., “Polaris-LAMP: Multi-Modal 3-D Image Reconstruction With a Commercial Gamma-Ray Imager,” IEEE Transactions on Nuclear Science
Notes: So first I’ll start with a brief introduction. Radioactive source imaging is an important task with many applications related to nuclear safety and security, such as accident remediation, lost source search, and accident response. And many different radiation imagers with different concepts have been developed in the past, such as Compton imager or coded aperture.
On the other hand, what we have today is this enormous advance in computer vision technology, such as Simultaneous localization and mapping, using lidar and stereo camaras.

## Slide 6
Single Detector Imaging - Introduction
Single detector
SLAM, Odometry
Scene Data Fusion (SDF)
Single detector
Single detector Free-moving 3D radiation imaging?
Inexpensive, less complicated electronics, rugged…
SLAM
Notes: So first I’ll start with a brief introduction. Radioactive source imaging is an important task with many applications related to nuclear safety and security, such as accident remediation, lost source search, and accident response. And many different radiation imagers with different concepts have been developed in the past, such as Compton imager or coded aperture.
On the other hand, what we have today is this enormous advance in computer vision technology, such as Simultaneous localization and mapping, using lidar and stereo camaras.

## Slide 7
100 distributed source
~100 s total measurement time
10 cm radius spherical detector
Single Detector Imaging - Introduction
Can we reconstruct the source image just by looking at the measurement?
Notes: So here is a simulated example scenario. A point source of 10 microcurie is placed in the middle of the imaging space, and it is marked with red x. We assume a constant background of 50 cps, and the detector is moving around, and the moving path is drawn with arrows, starting from the bottom left corner. The integration time is 0.1 second per measurement, so each arrow represents 0.1 second of measurement. And the arrows are colored differently, depending on the number of counts we get from the source in the middle. The variance in count rate is also shown in the figure bottom right. Here the x axis is the measurement number, and y axis is the number counts in each measurement.
And although here we are showing only 2-d image, the simulation was full 3d, so that the simulated space is 10x10x10m 3d space, and only the projection onto the xy plane is shown here. .
For image reconstruction, ML-EM algorithm is often a popular choice, so we can use MLEM algorithm on this data,

## Slide 8
Data vector
Image vector
System matrix
Single Detector Imaging - Introduction

## Slide 9
Data vector
Image vector
System matrix
Maximum likelihood — Expectation Maximization (ML-EM) algorithm update rule
Single Detector Imaging - Introduction
Maximum likelihood estimation (MLE) with the negative log-likelihood

## Slide 10
MLEM 200 iterations results.
A major failure!
Failure of ML-EM
Notes: And this I the reconstructed image we get after 200 iterations of MLEM algorithm. As you can see, the mlem algorithm completely fails to localize the source. And interestingly, the mlem reconstruction prefers images with high voxel values close to the moving path. Also, as you can see in the forward projection plotted in orange in the figure bottom right, there is some signs of the forward projection overfitting to the data.

## Slide 11: Gaussian Process Prior (GPP) Image Reconstruction

## Slide 12: Gaussian Process Prior - Introduction
Image pixels are not independent!
Pixels close to each other are more correlated than pixels afar.

## Slide 13: Gaussian Process Prior - Introduction
Image pixels are not independent!
Pixels close to each other are more correlated than pixels afar.
Using a Gaussian random field to model spatial correlation.
Gaussian process, Kriging
A Gaussian random field with local correlation

## Slide 14: Constructing a Gaussian Process Prior
Gaussian-to-exponential link function
Image vector is governed by a zero-mean multivariate Gaussian distribution
Hyperparameter determines “characteristic correlation length”
Squared exponential kernel
Hyperparameter determines the “mean pixel intensity”

## Slide 15: Constructing a Gaussian Process Prior
Image vector is governed by a zero-mean multivariate Gaussian distribution
Bayes’ rule in terms of the underlying variable
Prior distribution
Maximum a posteriori (MAP) formulation

## Slide 16
Gaussian Process Prior — Results
Ground truth

## Slide 17
Ground truth
MLEM reconstruction
200 iterations
Gaussian Process Prior — Results

## Slide 18
Ground truth
GPP reconstruction
,
Gaussian Process Prior — Results

## Slide 19
300 distributed source
Ground truth
Gaussian Process Prior — Results

## Slide 20
MLEM reconstruction
200 iterations
Gaussian Process Prior — Results
Ground truth

## Slide 21
Gaussian Process Prior — Results
Ground truth
GPP reconstruction
,
How much can we trust this image reconstruction?

## Slide 22: Bayesian Uncertainty Quantification

## Slide 23
Uncertainty — Bayesian Credible Interval
Bayes’ rule
Prior distribution
Likelihood
Posterior distribution
Notes: Showing the Bayesian form of posterior

## Slide 24: Uncertainty — Bayesian Credible Interval
In Bayesian statistics, credible intervals are often quoted to represent uncertainties.
Notes: Showing the Bayesian form of posterior

## Slide 25: Uncertainty — Bayesian Credible Interval
How can we find the credible interval, when the posterior is not analytically available?
Notes: Showing the Bayesian form of posterior

## Slide 26: Uncertainty — Bayesian Credible Interval
How can we find the credible interval, when the posterior is not analytically available? : Collect samples.
Notes: MCMC

## Slide 27: Uncertainty — Bayesian Credible Interval
How can we find the credible interval, when the posterior is not analytically available? : Collect samples.
Notes: MCMC

## Slide 28: Uncertainty — Bayesian Credible Interval
Posterior from the GPP algorithm :
Markov Chain Monte Carlo (MCMC) to sample from the intractable posterior
Notes: MCMC

## Slide 29: Laplace Approximation
Instead of sampling the posterior, we approximate the posterior
Notes: Laplace approximation

## Slide 30
Approximate the posterior with a multivariate Gaussian distribution
Laplace Approximation
Notes: Comparison between pcn mcmc and laplace’s approximation

## Slide 31
Laplace Approximation
Notes: Some more figures

## Slide 32
Bayesian UQ Can Be Done in Two Ways…
1. Sampling method
2. Approximation method
Slow, but more accurate
— Preconditioned Crank-Nicolson Markov Chain Monte Carlo (pCN MCMC)
Fast, but less accurate
— Laplace approximation
Notes: Some more figures

## Slide 33: pCN MCMC Uncertainty Quantification
Ground truth
GPP reconstruction
,
Notes: Laplace approximation

## Slide 34: pCN MCMC Uncertainty Quantification
GPP reconstruction
,
90% Bayesian credible interval
(pCN MCMC, 106 samples, ~45 min)
High uncertainties in the “unexplored regions”
High uncertainties around the source and low uncertainties along the path
Notes: Laplace approximation

## Slide 35: pCN MCMC Uncertainty Quantification
GPP reconstruction
,
Non-zero true source activities inside the red boundary (ROI)
Boolean map (pCN MCMC ~45 min)
Red : True value above the interval
Green : True value within the interval
Blue : True value below the interval
Notes: Laplace approximation

## Slide 36
Laplace Approximation Uncertainty Quantification
GPP reconstruction
,
90% Bayesian credible interval
(Laplace approx., ~0.5 s)
Notes: Laplace approximation

## Slide 37
Laplace Approximation Uncertainty Quantification
90% Bayesian credible interval
(Laplace approx., ~0.5 s)
90% Bayesian credible interval
(pCN MCMC, 106 samples, ~45 min)
Notes: Laplace approximation

## Slide 38
Laplace Approximation Uncertainty Quantification
Boolean map (Laplace approx. ~0.5 s)
Red : True value above the interval
Green : True value within the interval
Blue : True value below the interval
Boolean map (pCN MCMC ~45 min)
Red : True value above the interval
Green : True value within the interval
Blue : True value below the interval
Notes: Laplace approximation

## Slide 39
Ground truth
GPP reconstruction
,
Laplace Approximation Uncertainty Quantification

## Slide 40
Laplace Approximation Uncertainty Quantification
90% Bayesian credible interval
(Laplace approx., ~0.5 s)
GPP reconstruction
,
Notes: Laplace approximation

## Slide 41
Laplace Approximation Uncertainty Quantification
GPP reconstruction
,
Boolean map (Laplace approx. ~0.5 s)
Red : True value above the interval
Green : True value within the interval
Blue : True value below the interval
Notes: Caveat!

## Slide 42
Boolean map (Laplace approx. ~0.5 s)
Red : True value above the interval
Green : True value within the interval
Blue : True value below the interval
Laplace Approximation Uncertainty Quantification
Notes: Caveat!

## Slide 43: Simultaneous Spectral Decomposition and Full Spectral Imaging

## Slide 44: SRNL H Area Contamination Measurements
Savannah River National Lab (SRNL)
SRNL H-area
Fence
Forest

## Slide 45: SRNL H Area Contamination Measurements
H-area LiDAR point cloud map
58 CZT detectors
LiDAR
MiniPRiSM imaging system

## Slide 46: SRNL H Area Contamination Measurements
Elevated counts near the fence.
Is it the source signal or the background?

## Slide 47
SRNL H Area Contamination Measurements
“Waterfall plots” from the measurements
2-D time-energy count histograms

## Slide 48
Very low Cs137 662 keV photopeak counts
SRNL H Area Contamination Measurements
Multiple background spectral features

## Slide 49: SRNL H Area Contamination Measurements
Setting energy ROIs around 662 keV and reconstruct images to increase the signal-to-noise ratio

## Slide 50: SRNL H Area Contamination Measurements
GPP reconstructed images

## Slide 51
Full Spectral Imaging and Spectral Decomposition
Data matrix
Image matrix
System matrix
Photon emission E
Problem — Too large image matrix and the system matrix

## Slide 52
Full Spectral Imaging and Spectral Decomposition
Data matrix
Image matrix
System matrix

## Slide 53
Low-rank approximation of the image matrix
Data matrix
Images
System matrix
Components
Full Spectral Imaging and Spectral Decomposition

## Slide 54
Det. response
Decompose the system matrix A into the geometric efficiency matrix Ag and the detector response matrix R
Data matrix
System matrix
Images
Components
Full Spectral Imaging and Spectral Decomposition

## Slide 55
Bkg weights & components
Data matrix
System matrix
Det. response
Images
Components
The background can also be decomposed into different background components and their corresponding count contribution.
Full Spectral Imaging and Spectral Decomposition

## Slide 56
Bkg weights & components
Apply the GPP to the images, components, and the background weights
Data matrix
System matrix
Det. response
Images
Components
Estimating 4 matrices altogether!
Full Spectral Imaging and Spectral Decomposition

## Slide 57: SRNL H Area Contamination Measurements
Component containing the 662keV peak
Compton edge at 477 keV
Combined data with the GPP

## Slide 58
Component containing the 662keV peak
Compton edge at 477 keV
SRNL H Area Contamination Measurements

## Slide 59
Conclusions / Future works
Scene Data Fusion (SDF) enables imaging with a single detector, which has a significant potential impact on radiation safety and security applications.
The proposed GPP algorithm can significantly improve image reconstruction quality over the conventional reconstruction methods while providing the uncertainty quantification capabilities.
The full spectral GPP allows for radiation mapping in scenarios with very low Signal-to-Noise Ratio (SNR) measurements and dynamically changing backgrounds.
Currently, we are working on applying the framework to various related applications, such as medical image reconstruction and dose rate mapping within the Chernobyl NPP shelter object.

## Slide 60: Questions?