## Slide 1
U.S. MDP 20 T working group meeting
04/16/2024
20 T REBCO/Nb3Sn hybrid dipole
design study update
A.V. Zlobin

## Slide 2: Cable parameters
Cable Parameter | Cable 1 | Cable 2 | Cable 3
Superconductor | REBCO | Nb3Sn | Nb3Sn
Strand size, mm | 7.1 | 1.1 | 0.8
Cu/nonCu ratio | 0.5* | 1.0 | 1.1
Number of strands | 1 | 38 | 38
Cable width, mm | 7.1 | 21.5 | 15.7
Cable small edge, mm | 7.1 | 1.85 | 1.39
Cable large edge, mm | 7.1 | 2.05 | 1.58
Cable packing factor | 0.78 | 0.90 | 0.85
TST cable structure and cross-section
Cross-section of the insulated cable is 8 mm by 8 mm.

## Slide 3: Coil and yoke cross-sections
REBCO layers are made of individual turns.
Space between REBCO turns and Nb3Sn blocks is reserved for the SM structure.
Number of turns in L1-2/L3-4/L5-6/L7-8 is 8/16/51/70.
The coil ID and OD are 50 and 315 mm.
Yoke OD is 1500 mm

## Slide 4: Field harmonics and magnet main parameters
n | 3 | 5 | 7 | 9
bn, 10-4 | 1.6 | -5.38 | 4.40 | -0.49
Field harmonics at Rref=17 mm and B=20 T

## Slide 5: Magnet margin to quench
The margins to quench along the load line
  11.8% for REBCO
  10.9% for Nb3Sn L5-6 and 12.8% for L7-8.
The magnet critical current margin is 10.9%, determined by the Nb3Sn L5
3
28
34
Nb3Sn coils: Jsc= 825/1638 A/mm2

## Slide 6: Coil margin optimization
REBCO coil:
higher tape Jc
combining 4-, 5- and 6-mm wide tapes to increase the cable critical current
Nb3Sn coils:
higher Jc of Nb3Sn strands
higher Je by optimizing the Cu:nCu ratio
Further cable and coil optimization need to be done to increase and equalize these values for REBCO and Nb3Sn coils.
Chart: r/r_nom; Jc_nom/Jc; B/B_nom
| 1 | 0.9 | 0.8
 | 88.22 | 88.22 | 88.22
 | 89.14 | 88.39 | 87.63
 | 87.23 | 86.25 | 85.25
 | 89.14 | 87.86 | 86.74
 | 87.23 | 85.47 | 83.93
 | 89.14 | 87.12
 | 87.23 | 85.14
 | 88.22 | 86.02
 | 88.22 | 85.7 | 83.4
Present margin
Target margin

## Slide 7: Quench protection considerations
Can we protect magnet by dumping the stored energy only into Nb3Sn coils?
Can we provide QP system redundancy?
Coil average Tmax
W/l ~ 5 MJ/m
Jcu=825/1489 A/mm2
L# (bloks) | L5 | L6 | L7 | L8
N turns | 25 | 26 | 35 | 35
Nq turns | 204 (L5+L6) | 104 (L6) | 280 (L7+L8) | 140 (L8)
Tmax, K | 200 | 305 | 240 | 390

## Slide 8: Magnet parameter comparison
Parameter | REBCO/ Nb3Sn | Bi2212/ Nb3Sn
Nominal current Inom, kA | 14.90 | 13.45
Nominal bore field Bnom, T | 20.0 | 20.0
Coil nominal field Bnom, T | 20.34 | 20.04
Coil to aperture field ratio Bmax/Bo | 1.017 | 1.002
Magnet margin at 1.9 K, % | 10.9 | 13.2
Total HTS coil area, mm2 | 601 | 972
Total Nb3Sn coil area, mm2 | 3854 | 3110
Chart: Insulated cable cross-section (mm2)
| CT I | CT II | SMCT I | SMCT II | CCT | BL I | BL II | CC I | CC II | CC III | SMCT-BSCCO | SMCT-REBCO
HTS | 3241 | 1494 | 2091 | 1527 | 4490 | 1360 | 1500 | 1290 | 1154 | 1012 | 972 | 601
Nb3Sn | 2150 | 6106 | 3780 | 5148 | 4915 | 4740 | 4640 | 2326 | 2558 | 4191 | 3110 | 3770
Total | 5391 | 7600 | 5871 | 6675 | 9405 | 6100 | 6140 | 3616 | 3712 | 5203 | 4082 | 4371
Chart: Load Line Margin (%)
| CT I | CT II | SMCT I | SMCT II | CCT | BL I | BL II | CC I | CC II | CC III | SMCT-BSCCO | SMCT-REBCO
HTS | 18 | 21 | 22 | 20 | 14 | 21 | 22 | 13 | 13 | 15 | 16.2 | 11.78
Nb3Sn | 25 | 15 | 18 | 15 | 14 | 17 | 17 | 13 | 13 | 7 | 13.2 | 10.86
REBCO/Nb3Sn
B2212/Nb3Sn

## Slide 9: Summary and next steps
Complementary conceptual designs of a 20 T hybrid dipole based on REBCO and Nb3Sn shell-type coils with realistic SC parameters and 150 mm cold iron yoke are being analyzed.
REBCO/Nb3Sn dipole
  efficient design with small HTS coil
  10.9% load line margins at 1.9 K <= limited by Nb3Sn coils
    possibilities of increasing the Nb3Sn coil and total magnet margin to the acceptable level are being studied
SM elements are integrated in the coil cross-section to keep the mechanical stresses in brittle HTS and Nb3Sn superconductors within the acceptable limits.
Next steps:
  mechanical and quench protection analysis
  magnetic design optimization of REBCO/Nb3Sn dipole
  REBCO coil technology development – in progress