## Slide 1: babyMOSS FTBF test beam status update
Tucker Hwang, Danush Shekar, Zhenyu Ye
EIC/RNC meeting
21 May 2024

## Slide 2: Completed items
Full physical setup of beam telescope box complete
  Rough alignment of box + scintillators completed with laser system out-of-beam
  Remote control/monitoring for power supplies, moving table, DAQ computer confirmed
  Safety check complete
  Installation ready for data-taking
Standalone FW→SW→DAQ ready
  Resolved ssh connectivity issues from over the weekend
  EUDAQ installed but not integrated, Corryvreckan more difficult

## Slide 3: Plans for the next week
Beam turns on Tuesday 5/21 morning, reaching FTBF by Tuesday night/Wednesday morning
  Possibility of some beam overnight on Tuesday (if primary user decides)
  ORC (not us) scheduled for Wednesday 1pm, installation of other setups that morning
On an ideal schedule:
  Confirm alignment with hitmaps overnight Tuesday (beamspot on R2/3), make modifications as necessary
  Start data-taking Wednesday night
Data-taking
  Efficiency, spatial resolution vs. VCASB (threshold), all other settings at default
  FHR vs. VCASB out-of-beam, all other settings at default?
  Also works as stress test
  Add new plane after BASE test: cluster size over incident angle at default settings

## Slide 4: CERN beam test: Apr 2024
Adapting cosmics data analysis code for beam
  3 planes → 4 planes, spaced 1 inch apart
  Our telescope has 6 planes
  Stress testing the alignment procedure
Why not Corryvreckan?
  Has lots of capability + widespread use + fast + out of the box!
  (baby)MOSS has non-uniform pixel pitch, but reference arms in Corry require uniform pitch/resolution
  May be possible to focus the beam on one region+HU? Or only select tracks in the same HU
    Latter would require some pre-processing; former consideration of beam spot size

## Slide 6: Alignment procedure
Find midpoints from 4 layers pairwise, then connect with line
  Produces a “average track”
Collect residuals in given DUT layer (e.g. 0)
  Attach cut to remove bad fits (e.g. for layer 0, -0.05 < x < -0.01)
Send cleaned hit data to alignment algorithm
  MIGRAD minimizes sum of square of residuals in X, Y over all tracks
  16 free parameters: rotation in XY, shifts in X, Y, Z for each layer
    Possibly reduce this to 12?
With new alignment values, recalculate residuals in X and Y (true hits minus average track) for all tracks