## Slide 1: babyMOSS FTBF test beam status
Tucker Hwang, Danush Shekar, Zhenyu Ye
EIC/RNC meeting
4 June 2024

## Slide 2: FTBF telescope

## Slide 3: Studies for this beam test
Non-DUT planes fixed at VCASB=15 DAC:
Efficiency as function of VCASB, angle
Spatial resolution vs. VCASB, angle
Cluster size vs. VCASB, angle
FHR vs. VCASB (out of beam, all VCASB set to scan value)
N.B. VCASB ↑ = pixel threshold ↓
  VCASB in DAC units, conversion to e-

## Slide 4
60 deg
15 deg
90 deg
30 deg

## Slide 5: Alignment
“Garbage in, garbage out”
  We want clean, “real particle” tracks to use for alignment
  Sources of contamination: noise hit(s) accompanying real hit(s) + only noise hit(s) on some layer
Reduce “noise tracks” with event selection:
  Require: exactly 1 hit/layer, apply cuts on residuals with linear fit
Calculating residuals on unaligned hits:
  Replaced averaging method with SVD-based orthogonal regression fit to hit on each layer (7 total)
  Minimal reduction in calculation speed in alignment/resolution studies
  Possible Numba acceleration? To be investigated
Collect residuals in each layer
  Apply cut to remove tracks with noise hits (e.g. for layer 0, -0.05 < x < -0.01)
  No direct metric from SVD fit: cut on orthogonal distance to hits could work
Send cleaned hit data to alignment algorithm:
  Minuit minimizes sum of square of residuals in X, Y over all planes over all tracks
  Without plane rotation: 28 free parameters: rotation in XY, shifts in X, Y, Z for each layer
  With plane rotation: XY rotation; XZ rotation; X, Y, Z shift; X-Z rot. center (2) = 49 free parameters (42 with one plane fixed)
Recalculate hit positions in each plane with new parameters

## Slide 6: Resolution
Designate one plane as DUT, others as reference arms
Require tracks to have exactly 1 hit/layer, with wider residual cuts than in alignment
SVD fit to 6 non-DUT planes; residuals in X, Y in DUT
Sanity check for alignment: are residuals centered near zero?
Residuals std. dev. around 6-7.5 μm, translates to ~5.5-7 μm resolution
VCASB=15 all planes
All other settings default
90° angle

## Slide 7
From Danush Shekar

## Slide 8: Hits per event per plane vs. angle
VCASB=15 for ref. arms, 10 for DUT
Definitive trend to higher cluster size at steeper incident angle
90 deg.
30 deg.
15 deg.
From Danush Shekar

## Slide 9: Challenges during data-taking
Recurring power connection issues, appeared during initial commissioning with FHR scan
Manifests as USBError: Input/Output Error
Occasionally accompanied by current dropping to zero (normally 1.8-2.5A)
Interruptions/inefficiencies/unevenness in data-taking, up to outright power failures
Possible cause(s): weak/loose connections from power supply
  Ground/5V cables are daisy-chained, so loss of connection in one plane would lose power to the rest down the chain
Viable workarounds:
  Physically reaffirming power cable connections (orange board connectors, power supply connectors inside/outside box)
  Sanded down some solder connections (worked the best)
To be more fully understood, permanent solution to be found

## Slide 10: Plans
Analysis of remaining data
  Majority of analysis chain completed
  Remaining to-do tasks:
    Finalized alignment parameters for rotated DUT datasets
    Overall improvements to analysis chain (in backup)
    Clustering algorithms: edge vs. corner? Common/uncommon shapes?
Improvements to existing setup:
  Improved power connections: sanding down soldered connections, redoing them entirely…
  DUT rotation, scintillator shift had to be done by hand: remote-controllable table?
  Steep angles cause secondary particle showers from aluminum holders: large holder apertures?
Future: incorporation of LGAD for timing studies: late June-early July; Jlab test beam: early fall

## Slide 11: Backup

## Slide 12: Beam schedule
Beam to MTest Fri 5/24 ~1 PM
Primary users (beam profile control) swap every 12 hours (night vs. day shifts)
Some interruptions (e.g. linac filament) but relatively minor/short-term
Total: 5 shifts as primary user, 3 shifts as parasitic

## Slide 13: Improvements
With clustering algorithm: requiring one cluster per layer vs. one hit
Residual cut finder for alignment:
  Found by hand for now
  Misalignment produces shift+broadening/narrowing of Gaussian peaks in some random direction/magnitude
  Iterative procedure:
    Sample over wide range → identify highest peak → narrow search window around peak → try again until std. dev. is of ~ same order as window: set this as residual cut
Fit metric for SVD fitting
  Initial thought: total orthogonal distance to hits from line
  Can validate this by looking at distance distribution from tracks within a residual cut and not
Minimization for alignment
  Individual parameter optimization instead of simultaneous
  Not sure how it affects runtime, but only needed once per data set