## Slide 1: WANDA-24 Fusion Energy Science
February 2025
Michael Loughlin
Oak Ridge National Laboratory

## Slide 2: Nuclear Fusion
Magnetic confinement
Inertial confinement
Neutron production: 3.5×1020 neutrons/sec/Gigawatt of fusion power.
Tritium breeding is essential for the fusion economy. Tritium breeding ratio > 1.05.
Notes: All will generate neutrons and therefore activated materials and waste.
Tritium breeding is an essential part of the fusion economy.

## Slide 3: Radiation Responses for Fusion (Tokamak example)
Notes: Shielding
Tritium breeding
Shutdown dose rate
Activation
Nuclear Heating
Damage
Transmutation

## Slide 4: Tokamak materials
Plasma facing material: tungsten, boron
Blanket
  Tritium breeding
  Energy conversion
  Shielding
Divertor
  Tungsten
Vacuum vessel
  Steel
Coils
  Niobium-Tin
  REBCO
Cryostat and Thermal Shield
  Steel
  Silver

## Slide 5: Neutron Spectra

## Slide 6: WANDA -24

## Slide 7: Fusion Neutronics
8 recommendations:
  Sensitivity studies
  Evaluations to prioritize specific nuclides
  Benchmark experiments
  Provide summary of existing fusion relevant integral experiments
  High fluence source
  Work force development
  Fission/fusion information exchange
  A repository of the facilities available for nuclear data measurements/experiments should be created.
SHINE Technologies has demonstrated clearly visible Cherenkov radiation

## Slide 8: Tritium Production
5 recommendations
Narrow down the specific nuclear data inventory for breeder, multiplier and structural material
Assess data and predictions for tritium production
Build a path to integral benchmarks
Data exchange between fusion, defense and nuclear data communities
High performance computing including software development
Notes: 1. Can production processes or reactor materials be used to establish a source of tritium for fusion energy applications?
2. Which nuclear data are necessary to support testing and operation of breeder blankets?
3. Is the accuracy of nuclear data sufficient to predict activation of breeder blankets?
4. What are the uncertainties and sensitivities to the tritium breeding ratio?
5. Can nuclear cross sections be used to accurately predict transmutation of materials in blankets?

## Slide 9: Material Damage
7 recommendations
  Bridge transport and molecular dynamics
  Improve recoil distributions
  Recoil distribution sanity checks
  Scoping studies to prioritize material damage data
  Uncertainty Quantification
  Switch to arc-dpa metric
  Improve means to report issues to evaluators
Kmckiern, CC BY-SA 4.0 <https://creativecommons.org/licenses/by-sa/4.0>, via Wikimedia Commons

## Slide 10: Summary
Code development & Modeling
Benchmarks
ID important nuclides
Data Evaluation and UQ
Evaluate experimental facilities
Fusion Neutron Source
FPP
Discussion

## Slide 11: Further slides

## Slide 12: Fusion and Fission