## Slide 1: 20 T hybrid future activities
P. Ferracin
20 T hybrid Meeting
October 1st, 2024

## Slide 2: Towards 20 T hybrid magnet Overview
Three options considered (Cos-Theta, Block, Common-coil), all with a Bi2212 insert
Iterative process: magnetic, mechanical, and QP analysis
More focus on Cos-theta: MDP inserts and outserts current design
…and on common coils
  Only preliminary design with block
Quench protection of the 3 designs carried out
  Quench protection ok for 1+ m long magnet, for the 10-15 m length new solutions to be considered
HTS
LTS
HTS
LTS
HTS
LTS
R. Gupta and D. Martins Araujo, et al., 4LOr2B-02
Emmanuele Ravaioli, , et al., 4LOr1B-06

## Slide 3: Towards 20 T hybrid magnet Cos-theta option
Magnetic:
  2 layer HTS, 4 layer LTS, field quality and margin in spec, OR coil: 165 mm
Mechanics:
  Stress management required in all directions
    First 2 layers (HTS) with single cable in grove, second 2 layers (LTS) with single block in grove, last 2 layers traditional CT
  Coil stress acceptable, but very high stress in the mandrel (Inconel or Nitronic?)
  Large mechanical structure: 1120 mm.
    Pre-load provided by bladder and key support structure to reduce peak field in conductor.
Marika DAddazio, , et al., 4LOr2B-03

## Slide 4: Next steps
Fine tune of CT cross-section
  Reduce stress in some coil corners by splitting blocks
Continue mechanical analysis support structure
  Optimization key positions…..

## Slide 5: Next steps
Continue exploring CT 4 or 5 layer option
  The idea is to minimize the overall coil area

## Slide 6: Next steps
Baseline CT option with ESC
  Thick Cu ring between layer 2 and 3

## Slide 7: Next steps
Hybrid with CORC/STAR

## Slide 8: Next steps
All HTS with Bi2212 Rutherford cable and CORC/STAR

## Slide 9: Common coil
Still some high stress in the baseline design
Xplore asymmetric option
HTS
LTS

## Slide 10: Block design
Study what we could do with TFD as an outsert
HTS
LTS

## Slide 11: Updated roadmap (work in progress)