## Slide 1: UV Exposure Incident

## Slide 2
Researcher exposing samples to ultraviolet light from a mercury lamp for 5 minute intervals (9 exposures)
Inside were three germicidal 40 watt lamps, each with 11 watts of UV-C which remained on during the operation.
For each exposure, the worker to opened the cover, inserted or removed a cuvette and closed the cover.
Hazard warning labels had been lost when system was reconfigured.
The employee was not wearing protective eyewear.

## Slide 3
Define work
Identify hazards
Develop controls
Line management approval
Work within controls
Authorize workers
Activity Development
Implementation
LBNL Activity-based WPC
Hazard and controls had originally been correctly identified.
Important control was missing after reconfiguration (hazard warning)
Workers not properly trained to recognize the hazard.