## Slide 1: Waveform Digitization Hardware Options
Carl Grace 06/04/2025
Lawrence Berkeley National Laboratory
Hybrid Neutrino Detection Workshop – University of Pennsylvania

## Slide 2: Introduction
The key goals of front-end electronics are typically precise timing and energy measurements
  Other goals such as pulse-shape discrimination are common
Many ways to achieve fast timing in practice
  Leading-edge Discrimination + Time-to-Digital Converter (TDC)
  Constant-Fraction Discrimination + TDC
  Full-speed Digitization (Nyquist-Rate Analog-to-Digital Converter)
  Waveform Digitizer (also called Switched-Capacitor Array or SCA)
Often other features of the signal are needed beyond timing
Feature extraction can also be done in a number of ways
  Post-processing of raw full-speed digital data
  Online-processing (digital pulse processing)
  Shaping + lower-rate ADC
  Analog feature extraction
Choices involve complex tradeoffs between cost, size, power, scalability, area, and performance

## Slide 3: Introduction
Traditional data acquisition approach with independent timing and energy paths
Threshold
Threshold
TDC
(Clock)
+
-
ADC
~MHz
Stefan Ritt

## Slide 4: Direct Timing Measurement
Threshold
Single Threshold
“Time-Walk”
Multiple Thresholds
T1
T2
T3
T1
T2
T3
Inverter & Attenuator
S
Delay
Adder
0
Constant Fraction (CFD)
Stefan Ritt

## Slide 5: Digital Approach
ADC
FPGA
How fast of an ADC do you need?
Need to sample faster than 2X the highest frequency component in your signal
To first order, BW ~ 0.35/risetime. (so, for 1 ns tr, BW = 3.5 GHz, fsample > 7 GS/s)
Also need to account for dynamic range (10 - 12 bits, typically)
12-bit, 6+ GS/s ADCs are available, but extremely expensive
Also, better timing with multiple samples on the leading edge!
J.-F. Genat et al., arXiv:0810.5590 (2008)
Angelo Rivetti

## Slide 6: Commercial Ultra-High-Speed ADCs
Analog Devices AD9213
12 bits, 10 GS/s, 5.1 W, ~$1.0k/channel (!)
Texas Instruments ADC12DJ5200
12 bits, 10 GS/s,4.0W, ~$1.2k/channel (!)
Not practical for fast timing. Can be a useful approach in applications with relaxed requirements (e.g. Mu2e)

## Slide 7: How Can We Get Around This?
Monolithic Power Inc.
Key innovation in the Switched Capacitor Array (SCA) is decoupling the sampling and quantization processes

## Slide 8: Waveform Samplers – PSEC4
PSEC4 – U Chicago, Switched-Capacitor Array, 130 nm CMOS
< 100 ps sampling, 1.6 GHz BW. 6 channels, 256 deep analog memory
50 kevents/s, 16 mW/channel max, ~10 ps timing resolution, 1 W for 64 channels
Power-Hungry slope ADC
In a waveform digitizer you continually sample the input at high speed into an analog memory. When you get a trigger you read out with a slow ADC.

## Slide 9: Waveform Samplers – DRS4
DRS4 – PSI, Switched-Capacitor Array, 250 nm CMOS
200 ps sampling, 650 MHz BW, 9 channels, 1024 deep analog memory
~30 kevents/second readout, 33 mW/channel quiescent  2.1 W for 64 channels
~11.5 bits SNR, 5 ps timing resolution

## Slide 10: Practical consideration: SCA “Time Stretch Ratio”
Clock
IN
Out
dts
dtd
Typical values:
dts = 0.5 ns (2 GSPS)
dtd = 30 ns (33 MHz) → TSR = 60
Stefan Ritt

## Slide 11: TSR Leads to SCA Deadtime
sampling
digitization
lost events
sampling
digitization
Sampling Windows * TSR
Chips usually cannot sample during readout ⇒ “Dead Time”
Technique only works for “events” and “triggers”
Dead time =
Sampling Window ∙ TSR
(e.g. 100 ns ∙ 60 = 6 ms)
Stefan Ritt

## Slide 12: SCA Deadtime can be addressed
digitization
FIFO sampler becomes immediately active after hit
Samples are digitized asynchronously
“De-randomization” of data
Can work dead-time less up to average rate = 1/(window size * TSR)
Example: 2 GSPS, 10 ns window size, TSR = 60 → rate up to 1.6 MHz
Stefan Ritt

## Slide 13: Summary of a few SCAs
ASIC | Lab | Sample Buffer Size | Sampling Rate [GS/s] | Analog BW [GHz] | # of Channels | Dynamic Range [bits]
DRS4 | PSI | 1024 | 5 | 0.7 | 8 | 12
PSEC4 | U Chicago | 256 | 15 | 1.5 | 6 | 12
AARDVARK | Nalu | 30k | 14 | 2.0 | 8 | 12
FPS | LBNL | 90 | 32 | 8.2 | 4 | 10
Aardvark has deadtime-less operation capability up to 100 kHz (sample buffer size reduced in this mode)

## Slide 14: FastPulse Precision Sampler (LBNL 2025)
FPS-II – 65 nm, 4 mm2
Response to fast calibration pulse
45 elements of SCA
RMS noise ~550 µV
Measurement of FPS-I

## Slide 15: Another option: Analog Feature Extraction
We can extract relevant features directly from the waveform using analog techniques. This could be much lower power and more compact (to allow more channels in a given space).
This calculation can be done in the digital or analog domain.
Example application: Pulse Shape Discrimination
Widely used ”Q-ratio” approach.

## Slide 16: NeuPIX: custom analog PSD ASIC
Very simply, the NeuPix compares the area ratio between a long and short integration to determine if an incident particle is a fast neutron or a gamma.
Analog signal processing has potential for lower power operation relative to a digital processor coupled with a fast waveform digitizer.

## Slide 17: Yet Another Approach: Fast Discriminator w/ FPGA TDC
Uses internal FPGA resources to implement low-resolution ADC & TDC
Can implement many channels in single FPGA device  excellent for high-resolution, high channel-count systems
Can be complementary to analog feature extraction
Basic Cell
1024
CLK
Bank Ref
Signal In
Channel Ref

## Slide 18: FPGA timing
Virtex UltraScale (20 nm) XCVU440 | Average Power/channel @10 kevent rate (mW) | #Channels | #Bits | Logic Cells (k)
50ps, 1024 | 3 | 1400 | 1 | 6%
50ps, 1024 | 12 | 330 | 2 | 9%
50ps, 1024 | 32 | 120 | 3 | 12%
Virtex UltraScale+ (16 nm) XCVU13P | Average Power/channel @10 kevent rate (mW) | #Channels | #Bits | Logic Cells (k)
50 ps, 1024 | 2 | 700 | 1 | 9%
50 ps, 1024 | 9 | 160 | 2 | 12%
50 ps, 1024 | 23 | 80 | 3 | 15%
Low per-channel power dissipation possible

## Slide 19: SCA vs Analog Timing Considerations
How many channels needed in the system?
How much deadtime can you accept (or if none, what is the max average signal rate)?
What is the signal BW?
What is the sampling rate requirement?
How deep do the records need to be?
What are your cost constraints?
What are you size constraints?
…

## Slide 20: Conclusion
There are a number of useful approaches to fast timing that allow tradeoffs between a number of important parameters
Waveform digitization is a powerful technique to decouple sampling and quantization. Allows huge reductions in power dissipation and cost.
Analog techniques (such as leading-edge discrimination + TDC) can be simpler and more compact, but are not as flexible and don’t have as good performance
Analog feature extraction can allow customized processing of a waveform for a particular application with further reduced power and cost
Implementing the TDC in an FPGA can potentially reduce cost and power
The best solution could be a mix of these.

## Slide 21: Thank You
This work was supported in part by the U.S. Department of Energy under Contract No. DE-AC02-05CH11231