## Slide 1: LBNL Nuclear Data Measurements
T.A. Laplace et al.
Department of Nuclear Engineering, University of California, Berkeley
Nuclear Science Division, Lawrence Berkeley National Laboratory
WANDA 2026

## Slide 2: The 88-Inch Cyclotron at LBNL
K=140 sector focused cyclotron
Up to ~ 55 MeV protons/deuterons
Ion beams up to U
Neutron beams using thick target deuteron breakup

## Slide 3: Cave 5 / GENESIS
Deuteron beams ranging from ~14-55 MeV used for neutron production
Pulse Period of 100~170 ns
Pulse widths of ~5 ns @ 25 MeV
106 n/cm2/s at GENESIS target (~7 m downstream)

## Slide 4: Neutron beam characterization
Spatial distribution using scintillator on 2D stage
Flux and energy distribution using sTOF, validated using foil activation
24 MeV deuterons on C

## Slide 5: GENESIS measurements of (n,xγ) reactions
Modular array can be quickly re-configured
7 mechanically cooled HPGe (30% and 50%)
26 PSD-capable liquid scintillators grouped at specific angles (2-inch cylinders)
Full array modeled in Geant4. Simulation validated with gamma-ray sources and Cf-252

## Slide 6: GENESIS results
Isotope | Status | Supported by
C-12 | Gordon, J. M., et al. Phys. Rev. C 111 (2025) | NA-22
Na-23 | Gordon, J. M., et al. to be submitted to Phys. Rev. C | NA-22
Si-28 | Beam time March 2026 | NA-22
Cl-35 | Nagel, T. S. PhD thesis (2024) | DOE-NEUP & NA-22
Fe-56 | Gordon, J. M., et al. accepted in Phys. Rev. C | DOE-NE, NA-113 & NA-22
Nb-93 | Analysis in progress | SSAA
Bi-207 | Analysis in progress | SSAA
U-238 | Analysis in progress | DOE-NE, SSAA
12C(n,n’1γ) cross section
Gordon et al. PRC 111 (2025)

## Slide 7: Neutron detector response
Double TOF method developed at LBNL to measure particle specific light output in organic materials (proton & carbon)
Model independent method, no bias from multiple scatters
Results are also available at scintillator.lbl.gov
J.A. Brown, B.L. Goldblum, et al. Journal of Applied Physics 124, (2018)
J.A. Brown, PhD Thesis, UC Berkeley (2017)
T.A. Laplace, B.L. Goldblum, et al., Phys. Rev. C 104, (2021)

## Slide 8: Cave 0: Intense Fast-Neutron Source
In addition to GENESIS, LBNL possesses a second fast-neutron source, capable of operating at high neutron fluxes
  Current capability: Φ ≲ 1012 n/cm2/s, providing fluences relevant to fusion research with beam times on the order of hours
The source, located in Cave 0 of the 88-Inch Cyclotron, can be used thick-target activation, materials damage, and other integral measurements
  Recently employed for NIF-STARFIRE optics irradiation and neutron single-event effects testing of electronics
Existing TTDB target with cooling plate installed for continuous beam operation in Cave 0 shown at right 

## Slide 9: Cave 0: Intense Fast-Neutron Source
Thick-target deuteron breakup (TTDB) neutron spectra can be tailored based on the deuteron energy
  Neutron energies range from ~8 to 40 MeV, with spectra (shown in plot at right) dependent on the incident deuteron energy and angle relative to the beam1
     E.g., Ed = 33 MeV produces a forward (0°) neutron spectrum at peaked at ~14 MeV
Neutron beam has been characterized using both time-of-flight and foil activation methods
1. J. Morrell et al.,” Secondary neutron production from thick target deuteron breakup,” Phys. Rev. C 108, 024616 (2023). https://doi.org/10.1103/PhysRevC.108.024616
A new beryllium target, which should provide the capability to increase flux to Φ ≈ 1014 n/cm2/s while reducing the γ-ray dose, is under development with funding from the Missile Defense Agency 

## Slide 10: We’ve performed (p/d/n,x) isotope production cross section & decay measurements with LANL, BNL & Jülich
Beam
Al Degraders
Foil of Interest
Monitor Foils
g-ray
detector
Prostate : Müller, Cristina et al., JNM 58. 91S-96xaS (2017)
Isotope | Lead | Isotope | Lead
225Ac | Morrell | 68Ge/68Ga | Fox
134Ce | Morrell | 72Se/72As | Fox
Fe,Cu,Ti | Voyles | 193mPt | Ekeberg
160Tb | Chapman | 236Np/236Pu | Fassbender
86Y | Uddin, Martinsen | 117mSn/119mTe | C. Apgar
82,83,84Rb | Basunia, Uddin | 202Pb, 103Pd | Y.H. Lee
Hundreds of excitation functions have been measured and used to tune reaction modeling with results published in PRC, NIM, EPJ, Rad. Acta…
Including both 225Ac for which produced these impressive results AND the 68Ga used to produce these images!

## Slide 11: NEXUS (Neutron Experiments Under Soda) Pursuing research and innovation in neutron interaction studies, medical isotopes, and nuclear data
D beam
Tagged
Neutron
Cone
g-ray, neutron detectors
Sample
a
Scintillator/PMT
45°
Tagged neutron port in borated poly “doghouse”
Nexus removed from doghouse and rotated 45°
HPGe and scintillator detectors
API capability provides accurate flux determination
 Accurate mono-energetic measurement at 14.1 MeV, enabling independent normalization/comparison for other measurements like GENESIS
ZnO
scintillator
(a-detector)
45°
T Target
Sheilding
Microwave
focusing

## Slide 12: Stopping Power Measurements
Ions available in 10 MeV/u Cocktail beam
88” Cyclotron cocktail beams - variety of heavy ions to switch between on demand.
10, 16, 20 MeV/u variants with degrader foils to lower energy → can efficiently gather stopping power data at many energies for many ions
Time-of-flight energy measurement w/ movable scintillator. Particle arrival time distributions measured at two locations. Distributions compared to find phase delay.
Energies measured w/ & w/o target foil to determine energy loss

## Slide 13: Thank you!
This work was performed under the auspices of the U.S. Department of Energy by Lawrence Berkeley National Laboratory under Contract No. DE-AC02-05CH11231 and Lawrence Livermore National Laboratory under Contract No. DE-AC52-07NA27344. This work was supported in part by the U.S. Department of Energy National Nuclear Security Administration through the Nuclear Science and Security Consortium under Awards No. DE-NA0003180 and No. DE-NA0003996, and by the NNSA Office of Defense Nuclear Nonproliferation R&D through the LB23-GammaProdXSwithGENESIS-PD3Ob project, the NNSA Stockpile Stewardship Academic Alliance.
The initial development of the GENESIS array was supported by DOE-NE under the NEAMS and NEUP programs. Beamtime was supported by DOE/SC-NP Through the U.S. Nuclear Data Program.
Development of a high flux fast neutron source is supported by the Missile Defense Agency.
Isotope production cross sections are supported by the Isotope Program within the U.S. Department of Energy’s Office of Science.
The development of the DT-API capability is supported by the University of California, Berkeley.