## Slide 1
Integral Experiments for Criticality
An overview of the SPARC facility
Feb 2026
Nicolas Woolstenhulme1, Margaret Marshall1, Justin Johnson1, JD Kelly1, Troy Reiss1, Brad Benefiel1, Matt Lund1, Paul Ferney1, Catherine Percher2, Theresa Cutler3, Mathieu Dupont4, Will Wieselquist4, Andrew Barto5, and Don Algama6
1 Idaho National Laboratory
2 Lawrence Livermore National Laboratory
3 Los Alamos National Laboratory
4 Oak Ridge National Laboratory
5 Nuclear Regulatory Commission
6Deparment of Energy

## Slide 2: Lemmings, and Neutrons
Lemmings: Chaotic population cycle due to complex interactions in birth rate, vegetation growth, and predation in the sparse arctic
Modern transport codes are amazing, but unpinned by complex nuclear data for numerous reactions describing how nuclides & neutrons are born, bred, & lost
Zero-power criticals have always been indispensable in getting the balance right
So, it is with reactors. Neutron birth and death rates must be balanced within a small fraction of the total (<1%) to operate at stable power
And crucial in validating predictions to prevent “unintentional reactors” within economic fuel batch size (manufacturing, shipping, storage)
New fuels, materials, and cores: Advanced reactors further this enduring need

## Slide 3: A SPARC of Hope
Large-scale critical experiments crucially needed, the U.S. (and western world) has lost this capability
  Best met by a Horizontal Split Table (HST): The Swiss army knife of zero-power reactors
  Support licensing & deployment of LEU+ and HALEU fuel cycle (factory, shipping, reactor operation, and storage)
Historic HSTs in the U.S.
(all now decommissioned)
Fuels, moderators, reflectors
Fuels, moderators, reflectors
DNCSH supporting INL to deploy a new HST for HALEU criticality safety research
  Strong industrial support, direct relevance to executive orders
  PBF-613 (former SPERT-IV building) selected
  System Physics Advanced Reactor Critical facility (SPARC)
DOE/NRC Criticality Safety for Commercial-Scale HALEU Fuel Cycle and Transportation (DNCSH)
PBF-613
Rendering of HST in PBF-613
External Letters of Support
HST Design

## Slide 4: Facility Design
View from Main Floor
View from Basement
PBF-613
Basement of PBF-613
PBF-613 (former SPERT-IV reactor)
  Large “open basement”, low neutron room return
  Stout floors, overhead crane, radiologically clean
  Side wings for I&C, material storage
SPARC project scope includes:
  Safety basis creation for Hazard category 2 nuclear facility
  Install modular building with control console
  Install HST, I&C, and perform inaugural experiment

## Slide 5: Capability Plan
Deploying as soon as possible with minimum viable capability package
  Facility security posture for HALEU fuels and unclassified experiments
  HST can support up to 2m cube, 24 MT core
  “Open-source” mechanical fixturing design (threaded holes grid on table)
  Fuel and hazardous materials clad or contained
  Straightforward data and controls system (HST gap control, external neutron detectors)
  Ample space for storing moderators & materials
  Fuel storage area for UO2 RCF rods, U-Mo plates
Metal Hydride Heat Pipe Microreactor
TRISO Pebble Bed in Graphite Reflector
U-10Zr Metallic Fuel in SST Reflector, Fast Spectrum
Upgrades likely and/or feasible to come later
  Storage area suitable for beryllium
  Enhanced data and control system
    Data acquisition for heavily instrumented experiments
    Experiment electrical heating or chilling
    Remote controllable reactivity shims and/or oscillators
  Fuel storage racks for the full HALEU library
    TRISO compacts and/or pebbles
    UO2-in-poly blocks
    U-Zr metallic fuel
    Fueled salts, “other” uranium ceramics
  On-site gamma spectroscopy
  Suspect exhaust system for bare uranium
  Mode-switchable protocols for experiments with elevated information security

## Slide 6: Project Vision
Establish SPARC
-Design & build HST
-Create haz cat 2 safety basis
-Install control room/console
-Procure and install I&C system
First tests w/ RCF rods
Capability project funded by DNCSH
NNSA-NCSP Program Support
AFC-NGF Program, industry partnerships
2026
2027
2028
2029
NA-relevant crit. safety tests and training courses
NE-relevant reactor physics and crit. safety tests
Open for Business
Industry CRADA/SPP, DOE reactor programs, NSUF, potential new NE reactor physics & crit safety program
Coordinate and facilitate advanced fuels for SPARC
Ship RCF rods to INL
University Fuel Services
2030 →
PBF-613 maintenance
(repair roof, windows, lights, etc.)
INL-F&SS
Base operation and maintenance
IFM program support
In an era of many reactor projects
  SPARC is unique as a DOE-funded reconfigurable test reactor facility
  Earnest-but-balanced schedule while setting the stage for a multidecadal critical experiments faciltiy