## Slide 1: Fission Data Needs for Criticality Safety
Presented at the Workshop for Applied Nuclear Data Activities
Arlington, VA
Catherine Percher
February 11, 2026

## Slide 2: Nuclear Criticality Safety Art and Science of Avoiding Fission Chain Reactions in Handling, Processing, and Storage

## Slide 3: Fission Data Needs for Criticality Safety Ensure keff calculates less than an upper subcritical limit determined by critical data
234U | 235U | 236U | 238U | 237Np
238Pu | 239Pu | 240Pu | 241Pu | 242Pu
Most important: Fission cross section, nubar, and daughter neutron energy distributions for all incident neutron energies up to approximately 20 MeV
Burnup Credit- crediting spent fuel composition with reducing reactivity for back end of the fuel cycle operations (spent fuel pool, reprocessing, transportation, long-term storage)- 12 fissionable nuclides important to LWR fuel (see below)
  Fission product yields
Niche areas: neutron multiplicity distributions with neutron energy distribution (some subcritical simulations), prompt/delayed gamma data (accident doses)
Always need more validation benchmarks, particularly epithermal/intermediate. Colors in above table give relative benchmark coverage (darker the better)