## Slide 1: Gamma-ray and Neutron Beam Research Infrastructures at TUNL
Accelerator Facilities
High Intensity Gamma-ray Source (HIGS)
Laboratory for Experimental Nuclear Astrophysics (LENA)
Tandem Accelerator Laboratory
Research Areas:
Nuclear Structure and Fission
Nuclear Astrophysics
Low-Energy QCD
        Nucleon Structure
        Few-Nucleon Systems
By: Calvin R. Howell
Duke University/TUNL
Triangle Universities Nuclear Laboratory
Duke University, NC Central University, NC State University, and the University of NC at Chapel Hill
DOE Center of Excellence
Educates ~8% of the nation’s PhDs in experimental nuclear physics

## Slide 2: High Intensity Gamma-ray Source (HIgS)
1.2 GeV Storage Ring FEL
Features that enable basic and applied research
Wide beam energy range: 2 to 110 MeV
Selectable beam energy spread (by collimation)
High beam intensity on target (>107 g/s @ DE/E = 5%)
>95% beam polarization (linear and circular)
Example:
Ee = 800 MeV  g = 1566
lFEL = 193 nm
EFEL = 6.43 eV
Eg = 63.1 MeV
(2g)2
g-ray flux  Ie * Poc
Beam time structure:
T = 180 ns and Dt = 300 ps
Energy resolution by collimation
mirror
53 m
Enhancements underway
Upgrade of Linac RF system
FEL cavity mirror R&D

## Slide 3: HIGS: Beam Flux Performance and Requesting Beam Time
Requesting Beam Time
Nuclear Physics Research
  Proposals for beam time are reviewed by the HIGS Program Advisory Committee (PAC)
  PAC meetings are held about every 18 months
  PAC approved experiments are offered to scheduled for beam time within two years of approval
  An example of proposal solicitation is given at https://tunl.duke.edu/higs-pac-2025
Non-NP Projects
  Contact the TUNL Director

## Slide 4: Overview of Research at HIgS
HIgS operates about 1500 hours/year for nuclear physics research
Compton Scattering
nucleon electric and magnetic polarizabilities
nucleon spin polarizabilities
Few-nucleon Systems
photodisintegration of 2H, 3He and 3H (cross sections, target-beam helicity dependent cross sections, polarization transfer)
Nuclear Structure and Nuclear Astrophysics
NRF, (g,g’)
(g,n), (g,p), (g,a) and (g, fission) reactions
Figure from 2007 USA Nuclear Science LRP
Applied Research:
Nuclear Security
Medical Isotope R&D
g-ray Detector R&D
Low-Energy QCD:
Many-body Strongly Interacting Systems:
60 MeV ≤ Eg < 110 MeV
Eg ≤ 30 MeV

## Slide 5: HIGS: Layout of Target Rooms
g-ray beam
Beam flux monitors

## Slide 6: HIGS: Nuclear Resonance Florescence (NRF)
Elastic
Inelastic
Examples of angular correlations for elastic transitions
C. Iliadis and U. Friman-Gayer, EPJ A 57, 190 (2021).
1+/-
2+
0+
For a nucleus with a 0+ ground state, mainly spin-1 states are excited.
Elastic decays occur via gamma emission following well-defined angular distributions depending on the spin/parity of the state
Linearly polarized beam enables measurement of the parity, as well

## Slide 7: Clover Array at HIGS
8 clover-type HPGe
12 CeBr3 scintillators
Clover Array​
Beam direction: into page
Notes: Detectors in strategic positions to distinguish these patterns

## Slide 8: HIGS: Example of gamma-ray cascade measurement
Photon Strength Function
J. Isaak and N. Pietralla, Probing Nuclear Structure with Photon Beams, Handbook of Nuclear Physics, doi:10.1007/978-981-15-8818-1_2-1 (2022)
128Te
128Te
228Ac

## Slide 9: HIGS: NRF with radioactive targets
240Pu target (~4.7g)

## Slide 10: HIGS: Cumulative Fission Project Yield (FPY) Measurements via activation
g
Short-lived isotopes
Isotopes with medium length half-lives
145Ce
144Ce
Cumulative FPYs:
Monitor reactor operation
Post-event forensics
Calculation of n energy spectrum from reactors
g
239Pu*
34.8%

## Slide 11: HIGS: Cross-section Measurements Using Sample Activation Technique
Kollmorgen/Automations
Max linear speed = 10 m/s
Positioning precision = 33 mm
TUNL: Low-Background Counting Facility
Sub-basement of Duke Physics building
TUNL: RApid Belt-driven Irradiated Target Transfer System (RABITTS)
T1/2 > 20 minutes
1 second < T1/2 < 20 minutes

## Slide 12: HIGS: Facility and Research References
Facility:
NRF:
Activation:
I. Tsorxe et al., Measurements of short-lived fission product yields from photofission of 238U using 13.0 MeV monoenergetic photons, Phys. Rev. C 113, 024603, https://doi.org/10.1103/57zl-ks5z
J. Song et al., Photonuclear cross sections for 197Au: An update on the gold standard, https://doi.org/10.1103/PhysRevC.110.064604
Krishichayan et al., Fission product yield measurements using monoenergetic photon beams, 10.1103/PhysRevC.100.014608
S.W. Finch et al., Development of a rapid-transit system for precision nuclear physics measurements, 10.1016/j.nima.2021.166127
C. Sun et al., Energy and energy spread measurements of an electron beam by Compton scattering method, https://doi.org/10.1103/PhysRevSTAB.12.062801
H.R. Weller et al., Research opportunities at the upgraded HIS facility, https://doi.org/10.1016/j.ppnp.2008.07.001
W. Tornow et al., Measurement of magnetic dipole strength in 40 Ar between 9.3 and 10.3 MeV excitation energy and impact on neutral current neutrino interaction, Phys.Rev. C 112 (2025) 5, 054320, https://doi.org/10.1103/55xh-b4f7
O.Papst, Deviations from the Porter-Thomas Distribution due to Nonstatistical 𝛾 Decay below the 150Nd Neutron Separation Threshold, Phys.Rev.Lett. 135 (2025) 5, 052501, https://doi.org/10.1103/n6zw-zhz2
D. Savran et al., Transition width of the 𝐽𝜋 =1− two-phonon state of 88Sr, https://doi.org/10.1103/PhysRevC.110.024312
J. Kleemann et al., Gamma Decay of the 154Sm Isovector Giant Dipole Resonance: Smekal-Raman Scattering as a Novel Probe of Nuclear Ground-State Deformation, 10.1103/PhysRevLett.134.022503

## Slide 13: Tandem Accelerator Laboratory: Shared resource
Period: July 2017 – March 2020
Days scheduled = 698 (71% scheduled)
Total hours run = 8,873
Maintained by technical staff
Operated by researchers
Scheduled quarterly
Offers students hands-on holistic research experience: experimental nuclear physics + beam deliver optimization

## Slide 14: Tandem Accelerator Laboratory
Light-ion beams: p, d, 3He, 4He
Medium-mass ions: from SNIC
Secondary beams: n
Beam Injector Upgrade
(1) TORVIS: Toroidal Volume Ion
Source by the NEC
100 mA of H-
40 mA of 4He- and 3He-
Pulsed or DC
(2) SNICS II: Source of Negative Ions by Cesium Sputtering
SNICS II
TORVIS
Injector Line
Target Implanter
Station

## Slide 15: Tandem Accelerator Laboratory: Neutron Beam Areas
Neutron Source Reactions
En = 60 keV, 500 – 600 keV; 7Li(p, n)
En = 1 – 4 MeV; 3H(p, n)
En = 5 – 16 MeV; 2H(d, n)
Shielded Neutron Source: collimated beam
Open Neutron Source
Pulsed and DC beams available
Dtcp < 2.0 ns FWHM

## Slide 16: Tandem Lab: Example of n-n coincidence measurement
q1 = q2 = 40∘
En = 15.6 MeV

## Slide 17: Tandem Lab: Research Examples
Few-Nucleon:
Neutron-induced Fission:
Neutron Scattering:
M.E. Gooden et al., Energy dependence of fission product yields in the second-chance fission region, 10.1103/PhysRevC.109.044604
A.P.D Ram et al. Fission product yields from the 238U(n,f) reaction at En=4.6 MeV, 10.1103/PhysRevC.107.054608
R.C. Malone et al., Measurement of the 1S0 neutron-neutron effective range in neutron-deuteron breakup, 10.1016/j.physletb.2022.137557
R.C. Malone et al., Neutron-neutron quasifree scattering in neutron-deuteron breakup at 10 MeV, 10.1103/PhysRevC.101.034002
D. Cintas et al., Measurement of the sodium and iodine scintillation quenching factors across multiple NaI(Tl) detectors to identify systematics, 10.1103/PhysRevC.110.014613
W. Tornow, S.W. Finch and M.F. Kidd, Potential neutron-induced γ -ray background on natural tellurium relevant to
130Te 0νββ decay searches at the CUORE and SNO+ detectors, 10.1103/PhysRevC.103.044612
S. MacMullin et al., Measurement of the elastic scattering cross section of neutrons from argon and neon, 10.1103/PhysRevC.87.054613

## Slide 18: Support Acknowledgement
Thank you
Department of Energy, Office of Nuclear Physics
Grant #: DE-FG02-97ER41033