## Slide 1: Bremsstrahlung Measurements from the ECR Ion Source VENUS
Janilee Benitez
Lawrence Berkeley National Lab
April 7, 2020

## Slide 2
ECR Ion Source Basics
Why Bremsstrahlung Measurements?
Setup & Analysis
Results
Summary
Outline
Janilee Benitez NSD Talk April 7, 2020

## Slide 3: ECR Ion Source Physics
Plasma
Sextupole Magnets
(radial confinement field)
Solenoid Magnets
(axial confinement field)
µ-waves
gas
Ion
beam
3
1
2a
2b
4
High Voltage
5
1
+
3
+
2a
2b
4
gas
µ-waves
radial field
=
+
+
axial field
5
High Voltage
Ion beam
Key Ingredients
e-
ECR: Electron Cyclotron Resonance
Janilee Benitez NSD Talk April 7, 2020
BECR

## Slide 4: so
ECRs have been designed and built according to
Frequency Scaling:
Confinement Criteria:
Standard Model for ECR ion sources
Janilee Benitez NSD Talk April 7, 2020
LBL ECRs Generation | ωμ-wave | BECR | 16O6+ (eμA)
1st (1980s) | 6.4 GHz | 0.2 T | 80
2nd (1990s) | 14 GHz | 0.5 T | 800
3rd (2000s) | 28 GHz | 1.0 T | 4,000
4th | 56 GHz | 2.0 T | 10,000
4th generation ECR in design stages at 88” cyclotron
Z
BINJ
BEXT
BMIN
BECR

## Slide 5
ECR’s have been built according to:
Frequency Scaling
Confinement Criterion
Electron Heating
Janilee Benitez NSD Talk April 7, 2020
Generation | ωμ-wave | Max Inj. B-field | 16O6+ (eμA)
1st | 6.4 GHz | 0.4 T | 
2nd | 14 GHz | 1.7 T | 
3rd | 28 GHz | 4.0 T | 
Electrons absorb energy near the resonance zone
Simulations show more electron heating with shallower gradient (high Bmin/BECR).
Believed that shallow gradient means electrons spend more time near resonance and absorb more energy
Z
BINJ
BEXT
BMIN
BECR
shallow gradient
steep gradient

## Slide 6
Electron Energy Distribution
Janilee Benitez NSD Talk April 7, 2020
Ionization potential: how much energy electrons must have to ionize atoms
197Au59+ Ionization Potential~ 5.9keV
Optimum ionization cross section is ~5 x Ionization Potential
e-
e-

## Slide 7
Electron Energy Distribution
Janilee Benitez NSD Talk April 7, 2020
E
n (E)
Evidence that ECR plasma has 2+ Maxwellian velocity distributions
Relate the experimental distribution (bremsstrahlung spectrum) to the Maxwellian distribution by describing the plasma spectral temperature Ts
E
Counts/s
Ts=-1/slope
Cold
E~10s eV
Warm
10s eV <E < 5 keV
Hot
E > 5 keV
Studying Ts produced by hot electrons

## Slide 8: Setup for Bremsstrahlung Measurements
Plasma chamber
10 mm extraction hole
15.5 mm puller hole
Batman Analyzing Magnet
XR-100-CdTe Detector
Janilee Benitez NSD Talk April 7, 2020

## Slide 9: Extras
Calibration Applied
Spectra corrected for detector efficiency
Natural log of data taken in energy range of interest.
Linear fit applied. Ts=-1/slope
Bremsstrahlung Measurements Analysis
Janilee Benitez NSD Talk April 7, 2020
Chart: Energy (keV)
Chart: Energy (keV)

## Slide 10: Extras
Several ECR groups replicated results where Ts ↑ with Bmin/BECR
Previous Bremsstrahlung Measurements
Janilee Benitez NSD Talk April 7, 2020
Prior simulations had shown more electron heating with shallower gradient.
Previous measurements focused on comparing gradient at the resonance by changing Bmin/BECR
10
Shallow gradient
Steep gradient

## Slide 11: Extras
Bremsstrahlung Results
Varying Bmin
Janilee Benitez NSD Talk April 7, 2020
Vary Bmin & hold BECR constant
Bmin
Increasing slope with increasing Bmin
Significant effect on spectral temp Ts!
BECR
Surprising result! Long believed that Ts depended on BECR!

## Slide 12: Extras
Bremsstrahlung Results
Varying BECR
Janilee Benitez NSD Talk April 7, 2020
No change in slope with increasing BECR
No effect on spectral temp Ts!
Surprising result! Long believed that Ts depended on BECR!
Vary BECR & holdBmin constant

## Slide 13
Frequency (GHz) | Injection Gradient at BECR (T/m) | Extraction Gradient at BECR (T/m) | Ts (keV)
14 | -4.67 | 4.22 | 48.8
18 | -7.71 | 6.54 | 43.8
28 | -12.75 | 10.00 | 44.4
No change in slope with increasing different heating frequency
No effect on spectral temp Ts!
Bremsstrahlung Results
Varying Heating Frequency
Janilee Benitez NSD Talk April 7, 2020
Vary & holdBmin constant

## Slide 14
VENUS Only
Chart: Bmin (T)
Bremsstrahlung Results
Summarizing Data
Janilee Benitez NSD Talk April 7, 2020

## Slide 15
VENUS Only
Chart: Bmin (T)
| 0.74832519693233512 | 0.77011777370628631 | 0.80517741699114198 | 0.84005706127493862 | 0.87493670555873526 | 0.86587119829251136 | 0.88784377406752157
28GHz | 87.2164 | 73.1173 | 82.7368 | 88.9637 | 88.8327 | 100.3979 | 92.6424
28GHz | 80.0429 | 45.1264 | 40.1614 | 36.4191 | 35.2078 | 31.2901 | 28.2231 | 88.1983 | 43.8293 | 44.7984
28GHz | 80.2008 | 70.8643 | 70.0937 | 62.4801 | 54.9479 | 46.9854
18GHz | 42.7551 | 43.7902 | 38.4257 | 45.2684 | 61.6179 | 55.0435 | 46.5638 | 43.7902 | 27.1672 | 26.9 | 16.9186 | 19.1133
18GHz | 28.7056 | 56.8229 | 69.9772 | 34.2065 | 38.5177 | 31.1831 | 22.9485 | 30.1812 | 58.0357 | 46.3705 | 38.8736
14GHz | 60.1399 | 50.8263 | 42.3266 | 42.0853 | 34.6691 | 30.2701 | 30.6429 | 30.8807 | 27.8237 | 28.2187 | 29.9224 | 30.2709 | 29.9008 | 17.4843 | 42.1169 | 49.932 | 56.3297
14GHz | 34.6821 | 28.3644 | 27.8763 | 21.002 | 19.9885 | 34.6821 | 38.5407 | 38.9354 | 37.6577 | 36.3032
14GHz | 17.1213 | 18.5023 | 22.7216 | 22.7833 | 32.2079 | 10.4505 | 16.3532 | 17.1869 | 23.7959 | 24.5607 | 22.5752
Bremsstrahlung Results
Summarizing Data
Janilee Benitez NSD Talk April 7, 2020

## Slide 16
VENUS & AECR-U
& ECR
& SUSI
Chart: Bmin (T)
| 0.74832519693233512 | 0.77011777370628631 | 0.80517741699114198 | 0.84005706127493862 | 0.87493670555873526 | 0.86587119829251136 | 0.88784377406752157
28GHz | 87.2164 | 73.1173 | 82.7368 | 88.9637 | 88.8327 | 100.3979 | 92.6424
28GHz | 80.0429 | 45.1264 | 40.1614 | 36.4191 | 35.2078 | 31.2901 | 28.2231 | 88.1983 | 43.8293 | 44.7984
28GHz | 80.2008 | 70.8643 | 70.0937 | 62.4801 | 54.9479 | 46.9854
18GHz | 42.7551 | 43.7902 | 38.4257 | 45.2684 | 61.6179 | 55.0435 | 46.5638 | 43.7902 | 27.1672 | 26.9 | 16.9186 | 19.1133
18GHz | 28.7056 | 56.8229 | 69.9772 | 34.2065 | 38.5177 | 31.1831 | 22.9485 | 30.1812 | 58.0357 | 46.3705 | 38.8736
14GHz | 60.1399 | 50.8263 | 42.3266 | 42.0853 | 34.6691 | 30.2701 | 30.6429 | 30.8807 | 27.8237 | 28.2187 | 29.9224 | 30.2709 | 29.9008 | 17.4843 | 42.1169 | 49.932 | 56.3297
14GHz | 34.6821 | 28.3644 | 27.8763 | 21.002 | 19.9885 | 34.6821 | 38.5407 | 38.9354 | 37.6577 | 36.3032
14GHz | 17.1213 | 18.5023 | 22.7216 | 22.7833 | 32.2079 | 10.4505 | 16.3532 | 17.1869 | 23.7959 | 24.5607 | 22.5752
14 GHz- AECR-U | 38.7552 | 38.6987 | 40.4573 | 43.7338 | 46.2985 | 47.1861 | 46.4103 | 46.2491 | 43.6921 | 38.4303 | 17.9431 | 39.5429 | 40.91 | 40.01 | 41.09 | 40.4 | 39.49
6 GHz - ECR | 25.9 | 26.9 | 25.7
18 GHz - SUSI | 58 | 57.8 | 60.1 | 56.4
#
Ts is linearly dependent on Bmin not VBECR
Bremsstrahlung Results
Summarizing Data
Janilee Benitez NSD Talk April 7, 2020

## Slide 17
Chart: Bmin (T)
Bmin at 1.6 T | 186
Chart: Bmin (T)
4th generation ECR:
Want hot electrons to create high charge states
Engineering issues: plasma chamber damage and heat deposit into cryostat/magnets
Implications for Next Generation
Janilee Benitez NSD Talk April 7, 2020
LBL ECRs Generation | ωμ-wave | BECR | Bmin | Ts (keV) Bmin
2nd | 14 GHz | 0.5 T | 0.25 T | 30 keV
3rd | 28 GHz | 1.0 T | 0.5 T | 58 keV
4th | 56 GHz | 2.0 T | 1-1.6 T | 186 keV!
LBL ECRs Generation | ωμ-wave | BECR | Bmin | 
2nd | 14 GHz | 0.5 T | 0.25 T | 30 keV
3rd | 28 GHz | 1.0 T | 0.5 T | 58 keV
4th | 56 GHz | 2.0 T | 1-1.6 T | 186 keV!
LBL ECR’s Generation | ωμ-wave | BECR | Bmin | Ts (keV) Bmin
2nd | 14 GHz | 0.5 T | 0.25 T | 30 keV
3rd | 28 GHz | 1.0 T | 0.5 T | 58 keV
4th | 56 GHz | 2.0 T | 1-1.6 T | 186 keV!
LBL ECR’s Generation | ωμ-wave | BECR | Bmin | 
2nd | 14 GHz | 0.5 T | 0.25 T | 30 keV
3rd | 28 GHz | 1.0 T | 0.5 T | 58 keV
4th | 56 GHz | 2.0 T | 1-1.6 T | 186 keV!

## Slide 18
Ts increases with increasing Bmin (true for ECR’s min-B configuration)
Production of high charge state ions requires high density of hot electrons. How can we produce more for this purpose?
Implications for 4th generation (high frequency, higher Bmin)
Summary
Janilee Benitez NSD Talk April 7, 2020