## Slide 1: 88-Inch Cyclotron Updates
Janilee Benitez
November 4, 2025

## Slide 2: Layout
Cyclotron
The 88-Inch Cyclotron is fed by three ECR ion sources: ECR, AECR-U, and VENUS
Cave 4A Light Ion Facility
Cave 4B Heavy Ion Facility
ECR
VENUS
AECR-U
Where’s my beam!
88-Inch Layout
2
2
NSD Meeting - Nov 4, 2025 Janilee Benitez
2
beamtime:
I. radiation effects testing (~50%)
II. basic science (SHE search, neutrons) (~50%)

## Slide 3: Work at the ECRs*
*Electron Cyclotron Resonance
confining magnetic fields
plasma
ion beam
RF heating

## Slide 4
1st Generation ECR
1983
Max B-Field: 0.4T
Frequencies: 6.4GHz
Max Power: 0.6kW
2nd Generation AECR-U
1996
Max B-Field: 1.7T
Frequencies: 10, 14GHz
Max Power: 2.6kW
3rd Generation VENUS
2004
Max B-Field: 4.0T
Frequencies: 18, 28GHz
Max Power: 12kW
Beam Intensity ∝ ω2
4
4
ECRs at the 88”
NSD Meeting - Nov 4, 2025 Janilee Benitez
4

## Slide 5
ECR Source Usage at the 88-Inch
5
5
NSD Meeting - Nov 4, 2025 Janilee Benitez
5
E ∝ Q2
E=energy
Q=ion charge state

## Slide 6
1st Generation ECR
1983
Max B-Field: 0.4T
Frequencies: 6.4GHz
Max Power: 0.6kW
2nd Generation AECR-U
1996
Max B-Field: 1.7T
Frequencies: 10, 14GHz
Max Power: 2.6kW
3rd Generation VENUS
2004, 2008 for operations
Max B-Field: 4.0T
Frequencies: 18, 28GHz
Max Power: 12kW
Beam Intensity ∝ ω2
4th Generation MARS-D
Max B-Field ~ 6T
Max Frequency: 45GHz
6
6
ECRs at the 88-Inch
6
6
NSD Meeting - Nov 4, 2025 Janilee Benitez
6

## Slide 7: MARS
DOE funded: 1. winding of coldmass (sextupole + solenoids)
2. cryostat design
Largest risks for 4th Generation MARS
MARS-D R&D Project
1.1 Project Management
1.2 Project Design Documentation
1.4 Magnet Coldmass Design & Fabrication
1.6 Cryostat & Magnet in Cryostat Procurement
1.8 Ion Source Design & Fabrication
1.10 Beamline System Design & Fabrication
1.12 RF System Design & Integration
1.14 PLC System Design & Fabrication
1.16 Installation and Commission Prep.
1.17 MARS ECR Ion Source Installation
1.19 Test & Commission Final System
Sextupole (Closed-loop -coil)
Solenoids
Assembly
Test
Design
Fabrication
✔
~summer 2026
~summer 2026
closed-loop-coil
NSD Meeting - Nov 4, 2025 Janilee Benitez
7

## Slide 8
Adapted from Source: https://www.scientificamerican.com/article/superheavy-elements-are-breaking-the-periodic-table/
ECR
NSD Meeting - Nov 4, 2025 Janilee Benitez
8
The Role of ECRs in SHE Synthesis

## Slide 9
Element |  | Facility | Source | Beam | Target | Year
104 | Rutherfordium (Rf) | JINR, LBNL | PIG | 22Ne, 12C | 242Pu, 249Cf | 1964
105 | Dubnium (Db) | JINR, LBNL | PIG | 22Ne, 15N | 243Am, 249Cf | 1968
106 | Seaborgium (Sg) | LBNL ,JINR | PIG | 18O (54Cr) | 249Cf (Pb) | 1974
107 | Bohrium (Bh) | GSI | PIG | 54Cr | 209Bi | 1981
108 | Hassium (Hs) | GSI | PIG | 58Fe | 208Pb | 1984
109 | Meitnerium (Mt) | GSI | PIG | 58Fe | 209Bi | 1982
110 | Darmstadtium (Ds) | GSI | CAPRICE ECR | 62Ni | 208Pb | 1994
111 | Roentgenium (Rg) | GSI | CAPRICE ECR | 64Ni | 209Bi | 1994
112 | Copernicium (Cn) | GSI | CAPRICE ECR | 70Zn | 208Pb | 1996
113 | Nihonium (Nh) | Riken | 18 GHz ECRIS | 70Zn | 209Bi | 2004
114 | Flerovium (Fl) | JINR | ECR4M | 48Ca | 244Pu | 1999
115 | Moscovium (Mc) | JINR | ECR4M | 48Ca | 243Am | 2004
116 | Livermorium (Lv) | JINR | ECR4M | 48Ca | 248Cm | 2001
117 | Tennessine (117) | JINR | ECR4M | 48Ca | 249Bk | 2010
118 | Oganesson (118) | JINR | ECR4M | 48Ca | 249Cf | 2006
119 |  |  | AN ECR |  |  | 
120 |  |  | AN ECR |  |  | 
Electron Cyclotron Resonance Ion Sources
(ECRs)
Summary of SHE Production
9
9
NSD Meeting - Nov 4, 2025 Janilee Benitez
9

## Slide 10
Facility | ECR | Method | Production at source To-Date
JINR | DECRIS-PM (14 GHz) | MIVOC | 48Ti10+ 48Ti7+ ~30 uA/115 uA
GSI | CAPRICE (14.5 GHz) | High Temperature Oven | 50Ti8+ 90 uA
LBL 88-Inch Cyclotron | VENUS (28 GHz) | Inductive Oven | 50Ti12+ 200 uA
RIKEN |  |  | 
IMP CAFE2 |  |  | 
50Ti Production for SHE Searches
Courtesy of Damon Todd
3+ years developing beam
Continued Development of Inductive Oven (Damon Todd)
Delivered 23.5 µA on target!
10
10
NSD Meeting - Nov 4, 2025 Janilee Benitez
10
LBL BGS group will search for element 120 via:

## Slide 11: Cyclotron Upgrades

## Slide 12: Layout
Test Resource and Management Center (TRMC, DOD) funded upgrades
Goal: Improve production, transmission, and reliability of the 20 MeV/u cocktail
Why the need for 20 MeV/u cocktail?
layers on chips are increasing in thickness
increasing beam energy allows for deeper penetration into parts
Upgrades for Cocktail Delivery
12
12
NSD Meeting - Nov 4, 2025 Janilee Benitez
12
Xe46+
Xe43+
Success Criteria:
Cyclotron vacuum < 1.0x10-6 Torr
2. Delivery of 124Xe46+ with a minimum current of 20 epA

## Slide 13: Layout
Beam Production
Reliability
Transmission
M42
M41
Combo of improvements, reached KPPs
✓ <1.0 x 10-6 Torr
✓ > 20 pA Xe46+
Improvements affect several components
Know how to achieve reliably
Achieve reliably
Overall Picture of Upgrades
13
13
NSD Meeting - Nov 4, 2025 Janilee Benitez
13

## Slide 14: Layout
Improved vacuum system (necessary to transport the high charge state ion beams in the 20 MeV/u cocktail)
2. Spare He compressor (for use with LR1430 refrigerator)
3. Beamline power supply (replace a failed PS)
4. LN Line replacement (upgrade the LN delivery system to the cyclotron cryopanels and diffusion pumps)
5. Additional 18 GHz RF System (to generate required high charge state ion beams)
6. Improved VENUS Plasma Chamber (to run at higher power and improve reliability)
TRMC Project Activities
✔
✔
✔
✔
✔
14
14
NSD Meeting - Nov 4, 2025 Janilee Benitez
14

## Slide 15
15
15
NSD Meeting - Nov 4, 2025 Janilee Benitez
15
Combo of improvements, reached KPPs
✓ <1.0x10-6 Torr
✓ > 20 epA Xe46+
Cyclotron Vacuum is Important
Xe46+ 92 pA (from 10 epA)
Au53+ 100 pA (from 10 epA)

## Slide 16
Working around the 88-Inch
16
16
16
LN Vacuum Jacket Phase II Install
LN Vacuum Jacket Phase I Install
M41/M42 PS Install
LN Vacuum Jacket Phase I Install
M41/M42 Delivery
LN Vacuum Jacket Phase II Install
MARS Winding
M41/M42 PS Install

## Slide 17
Current Outlook for FY26
17
17
NSD Meeting - Nov 4, 2025 Janilee Benitez
17
Estimated 4,578 hours
DOE NP: 2,187 hours
BASE: 2,391 hours
  TRMC: 441 hours
  NASA: 441 hours
  Work For Others: 509 hours
  Blue Origin: 600 hours
  Alter Technologies: 400 hours
New for FY26
FY25 Q3, Q4 saw an up time of 99% and 98%

## Slide 18: Tite
Thank You
Any Questions?