## Slide 1
Diego Arbelaez
U.S. Magnet Development Program
MDP weekly meeting, 10/30/2019
First discussion on an updated Nb3Sn CCT Roadmap

## Slide 2: Introduction
CCT approach has been adopted as a method that provides stress management and simplifies the fabrication of superconducting magnets
Operation of model magnets with a bore field of ~ 9T and a large bore (90 mm) has been successfully demonstrated with CCT4/5
Program is currently focused on understanding training in these magnets with applicability to other magnet designs as well (especially those pursuing stress management approaches)
  Subscale magnet testing to improve understanding and develop new fabrication/assembly technologies
  Modeling efforts are ongoing to improve understanding of training sources and performance limits
Future model magnets will use input from subscale program and improved modeling approaches as well as input from HTS programs within MDP

## Slide 3: Nb3Sn Subscale CCT
Goals
Improve understanding of magnet mechanics and training behavior in stress-managed magnet approach
Provide feedback for magnet technology, modeling, and design at a rapid rate
Subscale Magnet Approach
Small standalone magnets (can be tested in small cryostat)
Take advantage of maximum pinning force for Nb3Sn conductors at lower field to operate at high Lorentz force
High Lorenz force + mandrel design choices  approximate stress in higher field magnets with similar margin
Subscale magnets will also be a testbed for novel instrumentation techniques (i.e. acoustics, quench antennas, fiber optic sensors, …)

## Slide 4: Improved Modeling of CCT
Stress management approaches to high field magnets add new interfaces between coil and support mechanism (e.g. channels in CCT mandrel)
Interfaces are usually not well defined since the interface stress may exceed the bond strength of the interface
Improved modeling is needed to understand the impact on the energy release and change in stress on the coils due to interface failure
Synergistic with material studies being performed within MDP

## Slide 5: Next “Large” CCT Model
Plan presented at previous MDP meeting
  4 layers
  Bore field of 12 – 13 T for standalone operation
  Bore diameter: 90 – 120 mm
Design study is required before finalizing parameters
Field strength and bore size needs input from HTS programs
Goals:
Demonstrate scale up for more than two layers
Demonstrate feasibility of CCT at higher field with a large bore

## Slide 6: Nb3Sn CCT as HTS Hybrid Outsert
It is important for the HTS programs to gain experience with applied external field (i.e. probe HTS magnet behavior at higher field and under higher stress)
CCT5 magnet has a large bore and moderate field strength (8.5 T with 90 mm bore) and is a possible candidate to do early hybrid testing
CCT6 would be designed to allow for hybrid testing with a higher field and/or bore size than CCT5

## Slide 7: Nb3Sn CCT Roadmap
2019 | 2020 | 2021 | 2022 | 2023
Subscale CCTs
Improved Modeling
CCT6 Design Studies
Possible Approach: CCT5 + HTS inserts
Nb3Sn CCT Program
CCT6 Fabrication and Testing
Possible Approach: CCT6 + HTS inserts
HTS Hybrid with Nb3Sn CCT outsert