## Slide 1: GARD ABP Workshop 1 (WG1): Lattice research needs of next-generation HEP facilities Valeri Lebedev
December 9-10, 2019

## Slide 2: Lattice Research Needs
Lattice design determines all main characteristics of accelerator, collider or storage ring
Present and future goals of beam physics
  Beam brightness increase (Grand Challenge #2)
    Luminosity, SR brightness, etc.
  Beam loss reduction (Grand Challenge #3)
    Reliability
    Serviceability
  Cost reduction
    Creates ways to higher energy, power, …
  Reliability improvement (other than beam loss)
  Energy (wall-plug) efficiency improvement
The past shows that new ideas are usually applicable to a wide range of accelerator types: e.g. strong focusing, …

## Slide 3: Why do we want High Beam Brightness?
Colliders
  Luminosity  1/s2
High power proton (ion) synchrotrons
  Small beam cross-section
    Reduces the cost
    Allows to focus the beam to small size on the target
    An increase of beam brightness may be the only choice for power increase if machine is already built
SR sources
  Increase the SR brightness
High brightness implies small transverse emittances However very small momentum spread typically is not required

## Slide 4: Main Barriers to Higher Beam Brightness
Instabilities
  A limitation at all high-intensity machines
Particle loss due to non-linearity of single particle motion, excited by beam space charge
  Important at
    low and medium energy high intensity accelerators
    beam-beam effects in colliders
Intrabeam scattering
  Important for colliders and storage rings
  Multiple IBS drives emittance growth
  Single IBS (Touschek) creates beam loss and non-gaussian tails

## Slide 5: General Requirements to the Next Generation Lattices
Goals
  High betatron tune (IBS,  instabilities, high transition energy)
  Effective chromaticity control at high betatron tunes
    Single particle stability (resonances),  instabilities
    Colliders: chromatic compensation of IR
  Large dynamic aperture
Means of achieving these goals
  Superperiodicity
  Optics integrability
  Lattices with strong x-y coupling by design
    Space charge tune shift, IBS
  Superior optics measurement and correction
  …

## Slide 6: Superperiodicity: Effective Means for Space Charge Mitigation
The tune shift due to beam-beam or space charge is typically limited to the total betatron tune shift for the entire ring
It should be counted per 1 period for superperiodic machines
Empirically, we know that superperiodicity helps (J-PARC)
Superperiodicity creates a possibility to increase greatly the beam brightness/intensity
  It is easier to achieve in a Rapid Cycling Synchrotron where beam stays at high tune shifts only for few thousand turns and only low order non-linearities play significant role
Modern instrumentation allows us to measure b-functions to ~1% accuracy
We need to achieve better understanding to what accuracy we need to build and tune machine optics to get “the expected” gain in beam brightness

## Slide 7: Optics Integrability
Main advantage: Creates a path to increase dynamic aperture
Challenges with present proposals
  Quite complicated beam optics
  High sensitivity to focusing errors
    Some integrable optics concepts are more sensitive than others
    Complications with chromaticity control
    High sensitivity to the beam space charge
New ideas are needed

## Slide 8: Lattices with High Betatron Tune
High betatron tune (i.e. small beta-functions) advantages
  Reduces  IBS
  Reduces  SR heating in electron storage rings/colliders
  Reduces growth rates of transverse instabilities
  Allows to reduce the vacuum chamber aperture and, consequently, the machine cost
What limits high betatron tune
  Reduction of dispersion function.
    Requires higher sextupole fields for chromaticity compensation
    limitation of dynamic aperture
We need to find how we could introduce suppression of chromaticity without compromising the dynamic aperture
  This may be part of research into optics integrability

## Slide 9: A couple of words about IBS
Above transition
  Mitigation of longitudinal IBS
    Lifetime growth proportionally to the momentum spread increase
      It is the only effective means
  Mitigation of transverse IBS
    Decrease of D2/b requires high horizontal tune
  Lattices with high betatron tune are required for the IBS mitigation
Below transition
  Quasi-equilibrium (qx ~ qy ~ qs ) may greatly reduce IBS
  Small beta-beating
  High horizontal tune to increase transition energy (if required)

## Slide 10: Where are we today?
Great progress in optics measurements and control
  Db/b  5-10%: Tevatron, LHC, …
  Db/b  1%: SR sources (electron rings)
  Tevatron optics model included x-y coupling, which could not be fully compensated with existing skew-quads
  FNAL high-energy cooler had strong x-y coupling by design
    Optics was fully measured and corrected
Superperiodicity tests – JPARC, PS Booster
Our proposal for EIC ring-based electron cooling has 100% x-y coupling by design
Integrable optics studies are carried out in IOTA (Fermilab)

## Slide 11: Synergies
This topic is quite universal. There are many potential synergies in this area with future BES and NP facilities.

## Slide 12: Timeline / Milestones
IOTA and UMER are built and represent good playgrounds for experimental studies for coming years
  IOTA has larger energy and supports studies both with proton and electron beams
Benchmarking of existing codes with experimental studies
Construction of small superperiodic ring with the goal to achieve the space charge tune shifts more than 1.

## Slide 13: Conclusions
The work on lattice research address all Grand Challenges of GARD ABP mission presented in the workshop template
Major directions for future developments in beam optics
  Superperiodic lattices
  Integrable optics
  Chromaticity control in lattices with high betatron tunes
  Optics measurements and control
Major fraction of experimental studies may be carried out at many existing machines
  While IOTA and UMER are the only machines built for such studies