## Slide 1: Nuclear Data Uncertainties for Advanced Reactor Applications
Bradley T. Rearden, Ph.D.
Director of Engineering
Presented to:
Workshop on Applied Nuclear Data Activities
March 4, 2020

## Slide 2: X-energy reactor solutions for different markets

## Slide 3: Established modeling and simulation capabilities are applied for design and licensing

## Slide 4: Depressurised Loss of Forced Cooling (DLOFC) without SCRAM from OECD Benchmark

## Slide 5: Applications of nuclear data uncertainties
Establishing possible ranges of quantities of interest (QOIs) (e.g. TSUNAMI/Sampler)
Establishing defensible bias and bias uncertainty for validation (e.g. TSUNAMI)

## Slide 6: Some quantities of interest
Enrichment, fuel fabrication, and transportation
  ~20% enriched 235U fuel and TRISO forms
Uncertainty margins for operational performance and safety
  Excess reactivity at startup
  Control rod worth for shutdown margin
  Power distribution
  Burnup
  Doppler feedback
  Xenon concentrations
  Radiation damage to components
Uncertainty margins for radionuclide source terms
  Fission products and other radionuclides
  Hardware activation
  Gamma production from fission and decay

## Slide 7: Areas of concern
Cross sections are tuned to integral keff benchmarks with little attention to accuracy of reaction rate predictions
Reaction cross section uncertainties are inconsistent with mean values used in design and safety analysis
Fission product yield uncertainties must be generated by code teams (e.g. ORIGEN)
Large changes in reaction cross sections in ENDF/B-VIII.0 make it difficult to use new data (e.g. reactor graphite thermal scattering data)
Lack of uncertainties for thermal scattering law data
Room temperature covariances are applied at all temperatures

## Slide 8
Clean • Safe • Secure • Affordable
X-energy develops Generation IV high temperature gas-cooled reactors (HTGR) and
TRISO fuel for advanced reactors world-wide.
J. Clay Sell, Chief Executive Officer

## Slide 9: Backup Slides

## Slide 10: Advantages of TRISO coated particle fuel

## Slide 11: Burnup and decay data are needed for fuel cycle analysis and radioactive source terms