## Slide 1: Advanced Detectors for XFELs and Proton Accelerators: Project Overview
Jen Bohon
January 25, 2019
LA-UR-20-20729

## Slide 2: High level view
3 years, commencing March 2020 ($3.76M)
Overarching goals:
  Development of diagnostics for high-repetition rate (GHz), high flux accelerators (focus on XFELs)
  Explore fundamental limits of Si and Diamond in this regime
  Application of these technologies to upgrade the Crocker Lab Cyclotron and the LANSCE accelerator
Approaches:
  Iterate simulation, fabrication and characterization of Si and diamond sensors and required readout electronics (lab and beam characterization)
  Perform radiation damage testing of devices
  Design and fabricate diagnostics for the proton accelerators

## Slide 3: Work Package 1 – Accelerator physics studies and development of the Crocker Nuclear Laboratory Cyclotron Facility
Goals:
  Develop, fabricate, install and commission an instrumented head (diamond detectors) for measurement of the transverse beam distribution on the new target for 211At production.
  Perform beam studies on the evolution of the beam (transverse and longitudinal) from the central region to the extraction radius.

## Slide 4: Work Package 2 – Developments in Sensor Fabrication for Diamond-based Diagnostics
Goals:
  Develop diagnostics capable of measuring the intensity, position, timing and profile of individual pulses for XFELs, the Cyclotron, and LANSCE
    For XFELs, targeting dynamic range over the full gain curve
    For proton facilities, targeting sufficient lifetime to enable practical use
  Transfer expertise in diamond device fabrication processes to LANL and the UC system (training of staff and students)

## Slide 5: Work Package 3 – Fundamental Limits in the Application of Solid State Sensors to Fast Beam Diagnostics
Goals:
  Explore fundamental limits in frame rate and dynamic range for single crystal diamond and silicon sensors
  Gain an understanding of radiation damage effects in diamond and silicon devices
    Hadronically-induced damage
    Electromagnetically-induced damage

## Slide 6: Work Package 4 – Beam-based Characterization and Validation of Prototype Systems
Goals:
  Characterize integrated (sensors with electronics) prototype devices with x-rays and protons
    Bring together collaborative team
    Photons:
      Synchrotrons (NSLS-II, CHESS, APS)
      XFELS (LCLS, SwissFEL, EuXFEL)
    Protons:
      UC Davis Cyclotron
      LANSCE WNR
  EM radiation damage testing at SLAC (or use of T506 target elsewhere)

## Slide 7: Timeline
Overall timeline as defined in the proposal
Training timeline:
  Simulation of sensors (UCSC and UCSB students/postdocs w/LANL, UCSC and UCSB staff): 3/20 – 3/21
  ASIC Design (UCD grad student w/LBNL and UCD staff): 3/20 – 3/21
  Rad damage experimental design (UCSB and UCSB grad and undergrad students w/ UCSC, UCSB, UCD staff): 9/21 – 9/22
  Beam tests and analysis (all students and staff): 3/21 – 9/22

## Slide 8: LANL, LBNL contributions
LANL:
  LANSCE beamtime (6 days per project year)
  CINT access (20 days per project year)
  Host and train 2 students up to 120 days per year
  5% FTE mentorship (John Smedley, DGL AOT-AE)
  Host annual collaboration meeting and support travel up to $25K/yr
LBNL:
  Host and train a UC Davis student
  Access to state-of-the-art electronics test and measurement laboratories
  Access to electronic design software

## Slide 9: Training and Dissemination
Student Training Notes:
  UCSC and UCSB graduate students to spend all three summers as well as two academic quarters (post-candidacy) at LANL
  UCD graduate student to spend time at LBNL
  Students will present work at conferences
  Try to involve undergraduate students where possible
Dissemination Notes:
  Publications
  Conference presentations
  Academic milestones for students