## Slide 1
Paolo Ferracin, Giorgio Ambrosio, Lance Cooley, Ramesh Gupta, Vadim Kashikhin, Alexander Zlobin
US Magnet Development Program
Area III: Technology
IIIa: Comparative analysis of magnet design concepts

## Slide 2: Proposed design studies roadmap
Title: Design studies of LTS/HTS hybrid magnets
  Focus on design of
    Outer (background) coils based on Nb3Sn superconductor
    Inserts based on
      Both with REBCO and Bi2212 superconductors
    Hybrid magnets towards 20 T field level

## Slide 3: Proposed design studies roadmap
Link with MDP areas and goals
  Task will be part of area III, with links to area I and II
    Area I  Nb3Sn
    Area II  HTS insert
    Area III  technology
      Modeling, diagnostics, instrumentation material
  The objectives will be in line with goal 2
    In particular the second part

## Slide 4: Proposed design studies roadmap
Time frame: 2020 – 2023
Methods
  Modeling effort
    “classical 2D/3D” mechanical, magnetic and QH simulations
      Developing new modeling techniques is not part of this task
      However, if new tool/analysis is required  feed-back to Technology area (III), modeling and simulations

## Slide 5: The LTS and HST roadmaps (presented yesterday)

## Slide 6: Hybrid program and goals of the design studies (I)
Hybrid program
  “Near term” (~2020-2022)
    CCT5
      8 T in 90 mm aperture
    CCT Bi2212 BIN5 and/or some inner coils from the CCT REBCO C2
      1-2 T field level
    Target hybrid field: ~ 9 T
Goals of the design studies
  Start analysis of challenges specifically of hybrid magnets
    Integration of LTS/HTS, mechanics, protection, powering, diagnostics, test facility…..

## Slide 7: Hybrid program and goals of the design studies (II)
Hybrid program
  “Medium term” (~2022-2024)
    CCT6 and/or SMCT
      11-12 T in 120 mm aperture
    CCT Bi2212 and/or SMCT Bi2212 and/or CCT REBCO and/or COMB REBCO
      Towards 5 T field level
    Target hybrid field: towards 14-15 T
Goals of the design studies
  Evaluate different designs (both LTS and HTS)
  Investigate alternatives (common-coil and blocks)
  Perform a comparative analysis in view of a 20 T hybrid magnet, considering both modelling and experimental results
    Margin, mechanics, field quality, quench protection strategies, fabrication-assembly-loading, performance of previous models, scalability, cost……
    Basically, help converging on all the and/or
  Continue the analysis of challenges specifically of hybrid magnets

## Slide 8: Hybrid program and goals of the design studies (III)
Hybrid program
  “Long term” (~2025 and beyond)
    Target hybrid field: towards 20 T
Goals of the design studies
  How much field from LTS and HTS respectively?
  Which design? How a 20T hybrid may it look like?
  Evaluation high Jc limitations in Nb3Sn
    We are working on very high Jc strands: can we afford it?
      Yes from the stress point of view (CCT and SMCT), but what about QP?

## Slide 9: Hybrid program and goals of the design studies (II)
Then, some personal thoughts on the comparative analysis….
    The goal should not be, or does not necessarily have to be
      reaching a consensus on a particular design
        ….historically, as far as I know, this goas has never been achieved before…
    Instead, more realistically, the working group could aim at
      Discussing and reviewing the different designs and listing pluses and minuses or open issues….grounding on “objective” criteria
      Providing inputs to the other areas (in particular area I and area II) to better define their roadmaps and overall directions, and avoid inconsistencies

## Slide 10: An example of comparative analysis from FCC/Eurocircol
Magnets at the limits of Nb3Sn superconductor
Based simply on modelling, the selection is very difficult
  Better if we rely also on experimental data

## Slide 11: An example of the hybrid challenges
FRESCA2 and Feather2
  13-14 T + 3-5 T
  work in progress at CERN
Significant challenges in mechanical integration
  Self supporting insert or in contact with LTS

## Slide 12: An example of the hybrid challenges

## Slide 13: Resources needed and possible timeline
Resources
  1.5 Post-Doc full time (0.5 per lab)
  0.5 FTEy for supervision and biweekly meeting of the working group
Timeframes and goals
  About 3-4 years in total
  First six months (by Sept. 2020)
    Review of work so far, by MDP and internationally (FCC/Eurocircol)
      Nb3Sn dipole magnets, HTS inserts, 15-20 T hybrid magnets
    Definition of a list of criteria and preliminary evaluation of MDP designs and/or proposed alternatives, always from the hybrid perspective
    Perform analysis in support of the test of the first hybrid magnet (9-10 T) with CCT5
  First year (by March 2021)
    Design study of second hybrid magnet (14-15 T)
      Based on CCT, SMCT and HTS development results and first hybrid test with CCT5
  Final goal
    Design study of a 20 T hybrid

## Slide 14: Appendix

## Slide 15: Show how the proposed roadmap builds off of MDP and international efforts to-date
Magnets at the limits of Nb3Sn superconductor
  Eurocircol/FCC design studies: margin

## Slide 16: Show how the proposed roadmap builds off of MDP and international efforts to-date
Magnets at the limits of Nb3Sn superconductor
  Eurocircle/FCC design studies: Jc

## Slide 17: Show how the proposed roadmap builds off of MDP and international efforts to-date
Magnets at the limits of Nb3Sn superconductor
  Eurocircle/FCC design studies: quantity of superconductor
No show-stoppers found in any particular design
  Peak stress <150 MPa at warm and <200 MPa at cold
No final selection (although CT as baseline)final choice