## Slide 1: Why use lumped-element methods or STEAM framework?
Daniel Davis,
Applied Superconductivity Center, National High Magnetic Field Laboratory, Florida State University, Tallahassee, FL, USA

## Slide 2: Contents
What is STEAM?
  My thoughts on its use
  What tools are in the network?
What is LEDET?
  What’s new in LEDET?
Applications of LEDET to Bi-2212, CLIQ, and solenoids/dipoles.
  i.e. examples from my PhD work

## Slide 3: STEAM

## Slide 4: Simulation of Transient Effects in Accelerator Magnets (STEAM)
https://espace.cern.ch/steam/_layouts/15/start.aspx#/
CO-SIM: Needed when individual tools can’t handle, or are inefficient, for a particular physics or scaling
  i.e. CLIQ in a novel circuit, mechanics during a heater protected quench
  Alternative would be something like multi-physics FEM, but solving times grow very quickly for these, especially if 3D geometry
  Co-simulation seems best for large scale or long term efforts that will be exploring many aspects of a magnet
  Individual tools can be used stand-alone (i.e. LEDET, BBQ) for “standard” magnet schemes
Setup is front-end heavy
Requires synchronized variable use
Once built, cases can be batch-run easily and new tool adapters are under development
L. Bortot, B. Auchmann, I. Cortes Garcia, A. Fernandez Navarro, M. Maciejewski, M.Mentink, M. Prioli, S. Schöps, A. Verweij, "STEAM: A co-simulation framework for modelling superconducting accelerator magnet circuits", accepted for publication in IEEE Transactions on Applied Superconductivity.

## Slide 5: Tool Summary
LEDET: Quench thermal and electrical transient solution for CLIQ, quench heaters, and simple energy extraction (dump resistor)
SIGMA: generates COMSOL portions of quench transient simulations
BBQ: conductor level quench transient analysis for finer levels of thermal detail
ProteCCT: CCT quench transient simulation utilizing an adjusted cos-theta model and a stand-alone inductance tool
COSIM: This is the tool for controlling multi-tool simulations
  Currently supports: QLASA, LEDET,comsol, PSPICE, LTSPICE
Forthcoming (SING): automated SPICE circuit model generator

## Slide 6
https://espace.cern.ch/steam/_layouts/15/start.aspx#/COSIM/Home.aspx
CO-SIM available?

## Slide 7: LEDET

## Slide 8: Lumped-Element Dynamic Electro-Thermal
Equivalent Circuit models for:
  Electrical (current, resistance)
  Thermal (heat, temperature)
  Magnetic (coupling currents, inductances)
Requires parametrized models of the behaviors of all system elements.
  For example, interfilament coupling currents use twist pitch and transverse resistivity
E. Ravaioli, B. Auchmann, M. Maciejewski, H. H. J. ten Kate, and A. P. Verweij, “Lumped-Element Dynamic Electro-Thermal model of a superconducting magnet,” Cryogenics, vol. 80, Part 3, pp. 346–356, Dec. 2016, doi: 10.1016/j.cryogenics.2016.04.004.

## Slide 9: Lumped-Element Dynamic Electro-Thermal
Freely distributed with acknowledgement & STEAM license agreement
  Tutorial and manual: https://edms.cern.ch/document/2046824
  Well supported by the CERN group (E. Ravaioli for LEDET)
    Executable so changes must be submitted, but I have multiple experimental features being explored
Essentially 1-2D  fast but only as good as the assumed relationships  Correction factors
Any non-linear features added significantly can slow down the simulation (example current sharing), but this can be optimized to reduce the impact.
  Non-linear features are added to specific cases to check for impact
Setup can be heavily automated and parametrized
Good for magnet designers who don’t spend a majority of their time on modelling

## Slide 10: Decouples the geometry from the transient simulation
Field constants in x and y (T/A) calculated once with your favorite tool (ROXIE, ANSYS, COMSOL, Biot-Savart)
Inductance calculated once with your favorite tool
  Linear magnets can be calculated by LEDET now (i.e. not solenoids or CCTs / yes common-coil & block)
  ROXIE, ANSYS, COMSOL, Biot-Savart
    Correction for iron is implemented as a correction factor as a function of current
Heat transfer – simplified nearest neighbors and helium cooling
Coupling currents – commonly used multi-filament twisted strand equations

## Slide 11: LEDET Simulation Example
Input Excel File
Parameters:
Conductor, Magnet
CLIQ, EE, Quench Heaters
LEDET Simulation Executable with archived print log, monitor time step and hot spot for quick debugging
Results
Analysis and Experimental Validation
Data can be obtained as a comma delimited text or MATLAB .m files
Top level results in an excel for all cases of a model for ease of comparison
*recent feature Automated PDF Reports
With key inputs, results, and plots
*new feature:
Interactive input file generator with visualization checks is a Anaconda Jupyter Notebooks

## Slide 12: Application Examples from my work

## Slide 13: Racetrack Geometry and Iron Field Contribution
10 kA Vapor Cooled Leads
Bi-2212 Racetrack in iron structure
RC6 Strand Margin to Current Sharing 75% Load-line Ic
Single Racetrack RC6

## Slide 14: RC-5: Quench Damage Deconstruction
Damage to RC5 coil due to an experimental test error that delayed quench detection and energy extraction at the start of measurements on the second cooldown to look at thermal cycling behavior.
L2-T1
L1-T6
L2-T1
L1-T6
L2-T1
L1-T6

## Slide 15: RC5: Delayed extraction led to a high MIITs quench
Detection system did not record a voltage rise.
  A voltage spike 150ms after transition began tripped the energy extraction
Simple sum of 1 kHz data
150 ms
Liquid Nitrogen Performance Before/After
Localized damage
MIITs (Deposited Energy)

## Slide 16: Adiabatic Quenched Turn Prediction
Calculates the Z-function of a typical Ag-sheathed
Bi-2212 round wire with a superconductor area ratio of 21% and a packing density as 100% inside 2212 filaments (50 bar HT OP samples)
Current drops linearly from 470 A per strand (7990 A cable) to 265 A (4505 A cable)
MIITs (Deposited Energy)
200 ºC

## Slide 17: Localized damage can be simulated with quench propagation and current sharing
With Current Sharing
and Quench Propagation
No Current Sharing
or Quench Propagation
RC5 High MIITs Quench
1 turn quenches at -85ms
NZPV 3 cm/s
Initial Quench Spot 1 mm
Lower voltage rise before time 0
Turns Quench All at Once
17

## Slide 18: RC7+RC8 Common Coil as a Quench Test-bed
Silver Mid-Tap
Common Coil RC7+RC8
Bladder
Key
Joint
Strain
Gauges
Double Pancake Windings

## Slide 19: Completion of a High Current CLIQ System at LBL
IGBT control of parallel capacitor bank triggering
System completed and validated on a room temperature resistor and then RC7+RC8 in liquid nitrogen
Capacitor Bank
CLIQ: Charged C → RLC Oscillation → dB/dt → Heat (Current Sharing) → Quench
Capacitor
Bank
High Current
CLIQ Unit
IGBT
CLIQ System Design and Assembly: Marcos Turqueti, Jordan Taylor, and Patricius (Rick) Bloemhard

## Slide 20: LBL-CLIQ Demonstration on RC7n8 Common Coil Dipole at 77 K
First CLIQ testing of a Bi-2212 dipole. Ready for liquid helium quench testing.
LEDET simulation matches reasonably with measurement.
  Rapid decay due to dynamic inductance replicated
High Current
CLIQ Unit
Further Testing Planned for May 2020

## Slide 21: Controlling CLIQ Heat Deposition with Mid-Taps: Coil Field and Quench Margin
Mid-Tap to Mid-Tap
Joint to Negative Terminal
RC7
RC8

## Slide 22: Where the margin is matters: Quench Margin Ranges, Geometry and Field
ecs [J/cm3] energy density margin to current sharing at I/Ic=0.75
eCS
[J/cm3]
eCS
[J/cm3]
eCS
[J/cm3]
eCS
[J/cm3]
w/ 7.829 T Background
RC-6
Self Field
w/ Iron Saturation
RC-7 &
RC-8
Sub-scale Accelerator
High Field Solenoid (Pup-4)
Notes: LEDET can be used to match CLIQ deposition with margin calculation to quickly find an efficient configuration.

## Slide 23: Quick to implement HTS behavior models
Voltage balance
Show LEDET changes to smooth transition of resistance
J = 660 A/mm2
0.8 mm wire
JE(4.2K, 5T)= 511 A/mm2
23
W/out
With
Random Examples

## Slide 24: Thank You For Your Attention!