## Slide 1: Inelastic Spectroscopy for Subsurface Exploration
Marie-Laure Mauborgne, R. J. Radtke, Fabien Haranger
Schlumberger
MMauborgne@slb.com

## Slide 2: What is Schlumberger?
Founded by a physicist and an engineer to conduct geophysical measurements of rock formations First measurement in 1927
Now
  82,000 employees >170 nationalities working in >120 countries
  >90 research and engineering centers worldwide
Notes: New numbers found on slb.com web page

## Slide 3: What Do We Do?
We develop tools to answer basic questions of oil exploration.
  Where are the hydrocarbons?
  What kind—oil or gas?
  How much can be extracted?
Use nuclear physics to measure
  natural radioactivity
  rock density
  hydrogen index, porosity
  rock matrix and pore fluid composition
  hole diameter
  Etc.
   Full characterization of the reservoir

## Slide 4: What Are Rocks Made of?
Rock = Matrix + Pores
Typical matrix materials
  In the reservoir — sandstone (SiO2), limestone (CaCO3), dolomite (CaMg(CO3)2)
  Everywhere else — “shale” (e.g., aluminosilicates)
Typical pore fluids
  Salt water (NaCl brine)
  Hydrocarbon (oil or gas, CnHm)
Notes: Very high overview of geology

## Slide 5: Tool Example: Dedicated to Spectroscopy
  Diameter: 4½ in (11.5 cm)
  Length: 9 ft (3 m)
  Mass: 300 lbm (130 kg)
  175°C, 20,000 psi rating (1,350 atm)
  Uses LaBr3:Ce spectroscopy detector
  Pulsed Neutron Generator, 3.6 × 108 neutron/s nominal output
  First (in the industry) in-situ measurement of total organic carbon (TOC)
  Tool used in this study
Notes: Count rate > 10Mcps

## Slide 6: Challenges
Not a laboratory environment:
  Temperature (150-200C)
  Shock (hundreds of g)
  Pressure (2,000 bar)
  Presence of corrosive fluids
High precision/accuracy measurements are required
  Rock density accuracy <1%
  Short acquisition time (from less than 1 s to about 1 min)
Logging While Drilling specificities:
  Space: less than 1% of the volume occupied by detectors
  Power: 90W for a nuclear tool with neutron generator and detectors
  Limited bandwidth for communication ~12 bits/s (mud pulse)
  Memory: ~2 GB for 300 h acquisition

## Slide 7: Recent Schlumberger-NASA Engagements—BECA
Proposal: Spectroscopy on Venus Lander to analyze its crust and look for water
Venus surface: P = 92 atm; T = 462ºC
  Operational lifetime: 2–4 h max.
  First test done at NASA Goddard Space Flight Center with an actual tool
  Very good results with only minor modifications of the tool
Notes: Bulk Elemental Composition Analyzer
IEEE 2016

## Slide 8: Recent Schlumberger Space Engagements—Dragonfly
In collaboration with Johns Hopkins Applied Physics Laboratory
Explore Titan (Saturn's largest moon) with an instrumented, radioisotope-powered dual-quadcopter
Provide pulsed neutron generator and expertise on gamma ray spectroscopy (capture and inelastic) to analyze the composition of the shallow subsurface

## Slide 9: Spectroscopy Measurement
Neutron-induced gamma ray spectroscopy with a neutron generator (dT)
Temperature up to 175C
Reconstruct lithology from elemental concentrations based on mineralogy models
Capture and inelastic gamma rays provide complementary information
Depth

## Slide 10: Why Do We Need Cross Sections?
Nuclear modeling is fundamental to well logging tool development
  Explore design choices quickly.
  Balance mechanics, electronics, and physics without costly experimentation.
  Complement and extend characterization measurements.
Accurate modeling relies on accurate cross sections.
For spectroscopy, better cross sections could
  improve elemental response (standard) derivation and interpretation algorithms
  allow elemental standards directly from modeling.

## Slide 11: Why Are Inelastic Gamma Rays Special?
Inelastic gamma rays provide:
unique information on carbon and oxygen
easier magnesium detection
complementary information on calcium, silicon, aluminum, sulfur, and iron
smaller sensitivity to chlorine.
A major drawback is the high background signal produced by the tool.
Being able to predict the amount of background is crucial to our application as well as separate elements found in the tool and the environment.

## Slide 12: Tool Background
Tool submerged in diesel
Measurement while the PNG is on only
Mixed capture and inelastic signal
Very distinguishable peaks for carbon and hydrogen
Issue to reproduce the real magnitude of the background from the tool
3x error

## Slide 13: Magnesium Inelastic
  ENDF/B-VI: Elemental cross sections
  ENDF/B-VII: Isotopic cross sections
    Finer binning of gamma ray energies but limited impact due to our detector resolution
    Missing line at ~1.8 MeV

## Slide 14: Silicon Inelastic
Use of natural compound in ENDF/B-VI, Si-28 afterward
Totally different response between ENDF/B-VI and newer releases
ENDF/B-VI in better agreement with our experimental results above 2 MeV

## Slide 15: Titanium Inelastic
Unfortunately, no experimental comparison
Better agreement between the latest ENDF version and the Baghdad Atlas

## Slide 16: Iron Inelastic
Very limited number of features on our experimental data
Mostly in agreement with Baghdad Atlas

## Slide 17: Calcium Inelastic
Calcium stays globally the same with some improvement in the sharpness of the peaks
Two peaks around 8 MeV disappeared
No experimental data at this energy

## Slide 18: Conclusion
Oilfield and space applications share an interest in lithology measurements obtained from neutron-induced gamma-ray spectroscopy
  Modeling is perfectly suited to help design such tools and understand their measurements
  Accurate cross sections are the foundation of this work. Major issues with inelastic cross sections are
    experimental measurements of inelastic gamma ray peaks above 4 MeV
    absolute cross sections for tool background.

## Slide 19: Related publications
  Impact of the ENDF/B-VIII.0 Library on Modeling Nuclear Tools for Oil Exploration, Mauborgne et al. Nuclear Data 2019 EPJ Web of Conf. Volume 239, 2020 – 20007
  Exploring for oil with nuclear physics, Mauborgne et al. Nuclear Data 2016 EPJ Web Conf. Volume 146, 2017 – 09009
  Designing tools for oil exploration using nuclear modeling, Mauborgne et al. Nuclear Data 2016 EPJ Web Conf. Volume 146, 2017 – 09036

## Slide 20: From Measurements to Elemental Standards
Focus on
  Si, Ca, Mg, Al, Fe, K, S, Na to identify rock matrix
  H, C, O, Cl to identify pore fluid
Extract the spectral signatures of the different elements
  Acquiring high-precision spectra in variety of environments
  Combining measured spectra to isolate specific contributions
  Guiding this process through modeling
High-quality elemental standards enable accurate spectral analysis, from which all tool answers are derived: elemental weight fractions, mineralogy, and total organic carbon