## Slide 1: Testing various yoke-pad configurations
Past analysis
  Fixed boundary displacement and ultra-rigid structure
    Acceptable stress distribution but unrealistic structure
  Realistic materials and open yoke/pad vertical interface
    Risk of over-compression of pole region during cool-down (coil ovalization)
    Tensile stress in the pole region to be investigated in 3D
Various yoke types motivation
  Performed in the past for CT but not for CCT or SMCT
  Goals
    Control of deformation after cool-down
    Minimizing tension when magnetic forces are applied
    Using bladder-and-key structure

## Slide 2: Various configurations Geometry and modeling
Model
  Simplified model
  Yoke/pad split into 8 pieces each
  Various configuration obtained with boundary conditions and node coupling
  Key between yoke/pad modeled with contact elements
Configurations
  Quadrupole structure (MQXF-like)
  Vertical split dipole structure
  Horizontal split dipole structure
  H-split yoke / V-split pad
  V-split yoke / H-split pad
1
2
3
4
5

## Slide 3: Various configurations Analysis summary
Quad structure
  Good control over cooldown deformation
  Lack of rigidity to counteract mag. forces
V-split dipole
  Risk of high stress / deformation during cool-down
  Some tension when magnetic forces applied
  Closing pad-pad interface might be the only solution to cool-down stress
H-split dipole
  Acceptable stress after cooldown but deformation contributes to magnetic forces stresses
  No control over stress when magnetic forces applied
V-split yoke/H-split pad
  Uniform radial deformation can be achieved after cooldown but ovalization needed to compensate for mag. forces
  Higher overall structure rigidity
  Lower tensile stress with hor. Interference
H-split yoke/V-split pad
  A lot of similarities to the case above
  Seems harder to control than the case above but it will be analyzed further

## Slide 4: Updated conductor properties
Elastio-plastic properties from Giorgio Vallone
  Based on MQXF cable modeling
Elastic material used for the initial optimization analysis
  Average of elastic and plastic parameters from the table
 | UNIT | RT | 4.5K
Ex | GPa | 31.95 | 30.00
Ey | GPa | 24.50 | 26.10
Gxy | / | 18.8 | 17.7
nu_xy | / | 0.2465 | 0.272
alpha_x | mm/m | 4.445 | 
alpha_y | mm/m | 4.115 | 

## Slide 5: Analysis, parameters and example result plot
Analysis Steps
  Room temperature preload
  Cool-down
  Magnetic forces
Varied parameters
Horizontal key interference
500 to 2000 um
Vertical key interference
0 to 450 um
Pad thickness
100, 125 and 150 mm
Horizontal key
Vertical key
Pad thickness
Bladders

## Slide 6: V-Split Yoke vs V-Split Yoke H-Split Pad V-Split Pad

## Slide 7: Conductor azimuthal stress Cool-down
Thinner (100mm) pad and 100-150um vertical gives the same benefits as thicker pad
Example case:
  Compression on mid-plane <100 MPa
With pad gap open, even 500um horizontal interference causes the compressive stress of ~150 MPa
Example case
  Compression <130 MPa
  450 um vertical key very difficult to insert in such configuration
Pad 100 mm
HK 1250 um
VK 100 um
Pad 100 mm
HK 250 um
VK 450 um

## Slide 8: Conductor azimuthal stress Magnetic forces
Corner artifacts
Example case
  Stress range after excluding artifacts
    +35 / -65 MPa
Tensile stress does not show high sensitivity on pad thickness nor vertical interfacernce
Pad 100 mm
HK 1250 um
VK 100 um
Pad 100 mm
HK 250 um
VK 450 um

## Slide 9: Mandrel stress Cool-down vs Mag. forces
Easier to achieve more balance mandrel stress/deformation
Example case
  RT < 234 MPa
  CD < 330 MPa
  MF < 387 MPa
Much higher mandrel stress and deformation
Example case
  RT < 177 MPa
  CD < 412 MPa
  MF < 469 MPa
Pad 100 mm
HK 1250 um
VK 100 um
Pad 100 mm
HK 250 um
VK 450 um
CERN measurement of Cu alloys (Rp0.2 at 4.5K)
CuAl10Ni5Fe4 C63000 nickel aluminum bronze 578 MPa
CuAl7Si, C64200 aluminum bronze 306 MPa
CuSn8P, C52100 phosphor bronze 247 MPa
CuSn5, C51000 phosphor bronze 315 MPa

## Slide 10: Summary and next steps
Symmetric pad/yoke interfaces allow to use the structure in two configuration
  Unique set key interferences required for each configuration
  Both configurations allow to minimize cool-down stress below ~100-130 MPa
    V-pad/V-yoke split structure: high vertical interference might not be possible
  Tension (local <40 MPa) still present in pole-turns in Magnetic Force case
  Local high stress in the key corners (structure, manageable)
  Shell stress in the range of 200-300 MPa
  Bladder operation analyzed for example cases
Further analysis
  Conductor contact elements implemented but de-bonded causes convergence problems
  Structure 3D model is ready to implement 3D conductor model (slice)
  Case with graded LD1 & MQXF will be investigated next
  Implementing SMCT coil geometry and performing geometry/preload evaluation
  Closed pad-pad interface in V-pad/V-yoke split structure

## Slide 11: Backup

## Slide 12: Shell Stress Magnetic forces
Stress in the shell below 300 MPa in both configuration

## Slide 13: Structure
High local stresses in pre-load key corners