## Slide 1
20 T Bi2212/Nb3Sn Hybrid
Common Coil Design with 15% Margin
Ramesh Gupta
November 2, 2021

## Slide 2: 20 T HTS/LTS Hybrid Common Coil Design
New hybrid designs for Bi2212 in series with Nb3Sn having 15%
All design use the Nb3Sn and Bi2212 Performance as of 9/29/2021
All designs are optimized for a good field quality
Configurations for 4 to 6 layers of main coil (+pole coil)
Space included for an intermediate mechanical structure for stress management (next step - optimize with proper analysis)

## Slide 3: Performance Assumptions of Nb3Sn & Bi2212
Nb3Sn
Nb3Sn
Bi2212
Bi2212

## Slide 4: Conductor Used
HTS - Bi2212
LTS - Nb3Sn

## Slide 5: September 2021 Design with New Jo
Bi2212
Nb3Sn
Mismatched Margins (new designs have matched margins – 15% over 20 T)

## Slide 6: 50 mm, 20 T Bi2212/Nb3Sn Common Coil
Bi2212
Bi2212
Nb3Sn
Nb3Sn
Nb3Sn
Structure
1 Layer of Bi2212
(+pole coils)
3 to 5 Layers of Nb3Sn
15% margin
20 T at ~14 kA
Space for structure (size to be iterated)
Full Model
One quadrant
(half of one side of the coils)
Several configurations with matched margin (15%) examined

## Slide 7
Configuration of September 2021
(mismatched margins with new J0)
New configurations (October 2021) with matched margins
(Number of turns gets reduced, in some cases number of layers as well)
Configurations Examined for Nb3Sn/Bi2212 Hybrids
All configurations have 1 layer of Bi2212 main coils and 6 turns of Bi2212 in pole coils
One layer of Bi2212
+Five layers of Nb3Sn
One layer of Bi2212
+Five layers of Nb3Sn
One layer of Bi2212
+Four layers of Nb3Sn
One layer of Bi2212
+Three layers of Nb3Sn
No. of turns: 336

## Slide 8
New configurations (October 2021) with matched margins
(Total number of turns gets reduced from 336, see also number of layers too)
Configurations Examined for Nb3Sn/Bi2212 Hybrids
No. of turns of Bi2212 per aperture = 74
No. of turns of Nb3Sn in 5 layers = 198
# of turns of Bi2212 per aperture = 80
# of turns of Nb3Sn in 4 layers = 188
# of turns of Bi2212 per aperture = 82
# of turns of Nb3Sn in 3 layers = 180
Total No. of turns: 262
Total No. of turns: 268
Total No. of turns: 272

## Slide 9: October 2021 Design #1 (6 layers in main coil)

## Slide 10: October 2021 Design #1 (margins for 6 layers in main coil)
Bi2212
Nb3Sn
New designs have matched margins – 15% over 20 T – in both Bi2212 and Nb3Sn coils for the reference Jo

## Slide 11: October 2021 Design #2 (5 layers in main coil)

## Slide 12: October 2021 Design #1 (margins for 5 layers in main coil)
Bi2212
Nb3Sn
New designs have matched margins – 15% over 20 T – in both Bi2212 and Nb3Sn coils for the reference Jo

## Slide 13: October 2021 Design #3 (4 layers in main coil)

## Slide 14: October 2021 Design #3 (margins for 4 layers in main coil)
Bi2212
Nb3Sn
New designs have matched margins – 15% over 20 T – in both Bi2212 and Nb3Sn coils for the reference Jo

## Slide 15: Summary
Three hybrid configurations optimized for Bi2212 in series with Nb3Sn having 15% margin for the reference J0 (Joverall)
They are ranging from 4 to 6 layers in main coil (+pole coil)
All designs are optimized for a good field quality as well
Common coil design is well suited for the very high field hybrid dipoles and seems to be more efficient than other designs. They also seem to need lower number of layers and less conductor
Space included for an intermediate mechanical structure for stress management (next step - optimize with proper analysis)

## Slide 16: Old slides from the last presentation in September 2021

## Slide 17
HTS
LTS
LTS
B0=20.03 T
Peak Enhancement
~2.2%
(low peak field enhancement)
50 mm, 20 T Common Coil Bi2212/Nb3Sn Hybrid Design
(Design Presented last time - September 2021)
LTS

## Slide 18
Field Quality in 20 T Common Coil Bi2212/Nb3Sn Hybrid Design (last September 2021 design)
All harmonics <10-4 (normal and skew)

## Slide 19
Bi2212
Nb3Sn
Splices in Common Coil Design
(between two single layer coil)
Perpendicular Nb-Ti splice in the low field region of BNL common coil dipole DCC017
In common coil design, splice (even between two types of coils), can be easily made in the middle of the coil where the field is very low

## Slide 20: Lorentz Forces @20 T in Bi2212/Nb3Sn Hybrid
Concept used in the earlier 16 T design for securing pole blocks

## Slide 21
A Few Possible Layout of Away Pole Coils Clearing Bore (others shown elsewhere)
CORC coil can be bent first away and then up/down
Practice & Tested Coils

## Slide 22: Key Benefits of the Common Coil Design for HTS/LTS High Field Hybrid Dipoles
Bpk=20.6 T
Bpk=16.5 T
Bpk=13.6 T
Natural segmentation between HTS and LTS (and different cables)
Easier tuning between HTS & LTS
Coil layers move as a module without causing strain at ends (BNL common coil had 200 mm)
Intermediate space for stress management structure. It can be easily adjusted, even at the late stage of the magnet construction