## Slide 1: CCT6 coil with contact elements and utility structure
Mariusz Juchno
2022-01-11

## Slide 2: Model geometry
Schematic view with exaggerated gaps
ANSYS geometry

## Slide 3: Contact elements between conductor and mandrel
Goal – simulating fully bonded and fully de-bonded case
Interlayer shim angle (optimization ongoing)
  Current angles (deg)
    45, 75, 80, 80
  Early indication: the closer to 90 deg the better
Radial coupling on the layer ID prevents convergence problems
  Details in backup
  Minor stress artifacts
azimuthal
azimuthal
radial
between layers

## Slide 4: Azimuthal Stress
Standard contacts
Bonded contacts
+10/-50 MPa?
+10/-100 MPa?

## Slide 5: Radial Stress
Standard contacts
Bonded contacts
+30/-10 MPa?
+10/-70 MPa?
+60/-10 MPa?
+50/-70 MPa?
Stress artifacts due to coupling

## Slide 6: Radial displacement (wrt undeformed RT geom.)
Standard contacts
Bonded contacts
+77 um
-1007 um
-77 um
+328 um
-1071 um
-76 um
-866 um
-817 um
Underestimated L1 mandrel rigidly and 45deg shim

## Slide 7: Mandrel stress (azimuthal)
Standard contacts
Bonded contacts
Underestimated mandrel rigidity in 2D 3D analysis needed

## Slide 8: Mandrel stress (azimuthal, shims angle, bonded only)
Shim analysis in progress
Current shims
  Angles (deg) 45, 75, 80, 80
  Stress (MPa) CD -318/+134, MF -344/+210
Best case
  Angles (deg) 90 in all layers
  Stress (MPa) CD -301/+98, MF -325/+243
Bonded contacts

## Slide 9: BACKUP

## Slide 10: Alternative method of constraining the conductor motion
Shim geometry +/- angle
Shim material G10
No fake shim to constrain conductor motion
Conductor and rib node are coupled on the layer OD
  Nodes CSYS rotated to cylindrical with NROTAT
  ONLY UR is coupled (UX for a CSYS 1 oriented node)
  All conductors except pole-turn have 2 nodes (pole-turn conductor only 1)