## Slide 1: Nuclear Data for High Energy Ion Interactions and Secondary Particle Production Applications: Semiconductors
Robert Reed
Vanderbilt University
Nashville, TN
Mar 1st, 2022
Support provided in part by NASA, DTRA, DoE, and others

## Slide 2: Basic Mechanism for Radiation-Induced Effects on Semiconductors
Total Ionizing Dose (TID)
J.L. Leray, Notes from 1999 IEEE Nuclear and Space Radiation Effects Conference Short Course
Displacement Damage (DD)
P.J McNulty, Notes from 1990 IEEE Nuclear and Space Radiation Effects Conference Short Course
P.W. Marshall and C.J. Marshall, Notes from 1999 IEEE Nuclear and Space Radiation Effects Conference Short Course
Single Event Effects (SEE)

## Slide 3: Radiation Transport Modeling for SEEs in Semiconductors Devices and Circuits
Active
Silicon
Primary Ion
Trajectory
Range-energy tables:
Requires Monte Carlo Modeling

## Slide 4: Monte Carlo Method Using High Performance Computing

## Slide 5: Monte Carlo Method Using High Performance Computing
Aix-Marseille University and CNRS, Marseille, France
CEA, Arpajon, France.
French Aerospace Laboratory (ONERA), Toulouse, France
STMicroelectronics, Crolles, France
Université Montpellier II, France
Soreq NRC, Israel
ESA-ESTEC, Noordwijk, The Netherlands
Chalmers University of Technology, Gothenburg, Sweden
Kallisto Consultancy Ltd., Guildford, United Kingdom
RadMod Research Ltd., Surrey, United Kingdom
Clemson University, Clemson, SC, USA
E.M.P. Consultants, Gaithersburg, MD, USA
IBM, Yorktown Heights, NY, USA
Jet Propulsion Laboratory Pasadena, CA, USA
NASA Johnson Space Center, Houston, TX, USA
Vanderbilt University, Nashville, TN, USA

## Slide 6: VU Code: Monte Carlo Radiative Energy Deposition (MRED)
Integrates the physics processes associated with the Geant4 toolkit with Fortran codes:
  CEM03 (protons) and LAQGSM, both nuclear physics codes
  PENELOPE 2008, an electron transport code
MRED was designed and written by Robert A. Weller and Marcus H. Mendenhall
MRED development as an engineering tool was frozen 2015

## Slide 7: Process Details – MRED
Kevin Warren, Ph.D. Dissertation, Vanderbilt, 2010

## Slide 8: Defining Sensitive Volumes
TCAD Derived Locations
Substrate
Sensitive
Volume(s)
Simple Sensitive Volume not appropriate
Keven Warren, Ph.D. Dissertation, Vanderbilt, 2010

## Slide 9: Results
Calibration with Heavy Ion
Prediction of Proton Response
Keven Warren, Ph.D. Dissertation, Vanderbilt, 2010

## Slide 10: Complex Material Systems
Ion-Ion nuclear reactions in non-silicon material near the sensitive volume contribute to the soft error response
To date, this is only important for radiation harden circuits
IEEE Trans. Nucl. Sci. : Warren et al. 2005, Dodd et al., 2007, Reed et al. 2007
Experimental evidence for this effect on a CMOS SRAM
http://images.dailytech.com/nimage/4621_21476.jpg

## Slide 11: Observed and Predicted SEU Rate for a RAD-HARD SRAM
SRAM used on NASA MESSENGER spacecraft
Observed Average SEU Rate:
  1x10-9 Events/Bit/Day
Vendor predicted rate using CREME96:
  2x10-12 Events/Bit/Day
  Classical Method nearly a factor 500 lower than observed rate
MRED-based predictions bound problem
Reed, IEEE Trans. Nucl. Sci., 2007

## Slide 12: Gaps:
https://en.wikipedia.org/wiki/Demosaicing.
Complex systems
Often the gap in knowledge is associated with the microelectronic device response to an irradiation
Nuclear Reactions
  Is nuclear data sufficient to cover all relevant materials used in IC manufacturing?
  Are models sufficient to capture reaction product distributions?
    Species, angle, and energy
Fission products for certain materials not defined in models (see talk by Tom Turflinger 10:10 am on Mar 3rd)
High-Energy Heavy Ion Test Facility !!!